Annex VII

### BID/PROPOSAL SUBMISSION FORM

To: 	UNDP Moldova,

131, 31 August 1989 Street, MD-2012 Chisinau, Republic of Moldova

Attention: Registry Office/Procurement

Dear Sir / Madam,

Having examined the Bidding Documents, the receipt of which is hereby duly acknowledged, we, the undersigned, offer to supply and deliver “Integrated Solution for Server Cluster and Storage /Parliament Project/ UNDP Moldova” in conformity with the said bidding documents for the sum of [total bid amount in words and figures] as may be ascertained in accordance with the Price Schedule attached herewith and made part of this Bid.

We undertake, if our Bid is accepted, to deliver the goods in accordance with the delivery schedule specified in the Schedule of Requirements.

We agree to abide by this Bid for a period of 120 days from the date fixed for opening of Bids in the Invitation to Bid, and it shall remain binding upon us and may be accepted at any time before the expiration of that period.

We understand that you are not bound to accept any Bid you may receive.

Dated this . . . . .day of . . . . .[year].

. . . . . . . . . . . . . . . . . . . . . . . . .			. . . . . . . . . . . . . . . . . . . . . .

Signature 						[in the capacity of]

Duly authorised to sign the Bid for and on behalf of . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Annex VIII

PRICE SCHEDULE

- The Price Schedule must provide a detailed cost breakdown for each item.

- Technical descriptions for each proposed item must provide sufficient detail to allow the Purchaser to determine compliance of Bid with specifications as per Schedule of Requirements and Technical Specifications of this ITB.

- All prices quoted shall be in US Dollars and shall be exclusive of all direct taxes, since the United Nations, including its subsidiary organs, is exempt from taxes. Other currencies shall be converted into USD at the UN Operational exchange rate on the day of competition deadline.

- The format shown on the following pages should be used in preparing the Price Schedule. The format uses a specific structure which may or may not be applicable but are indicated to serve as examples.

Name of Bidder ………………………………………

| Item # | Item Description | Required specification | Unit Price* | Quantity Required | Total Price per Item |
| --- | --- | --- | --- | --- | --- |
| I | Main Server |  |  | 2 |  |
|  | Form Factor: | Rack mount; 4U; Sliding rails and cable management arm | Offered Specification |
|  | CPU: | Four Intel Xeon Six-Core Processor E7540 2.GHz | Please, include detailed specification of offered equipment here. |
|  | RAM: | 32GB (8x4GB) PC3-8500 DDR3 1066MHz RDIMM RAM; Advanced ECC; 64 memory slots max. |  |
|  | HDD: | Two 146GB 2.5”Hot-Swap 10K 6Gbps SAS; Eight disk bays |  |
|  | Internal RAID: | RAID 0, 1 |  |
|  | PCI Slots | Four available PCI Express slots, incl. one x16 |  |
|  | Ports: | At least one front and one internal USB ports |  |
|  | Host Bus Adapters: | Two 8Gbps Single-Port FC HBA Adapters |  |
|  | LAN: | Four Gigabit Ethernet ports; load balancing and failover |  |
|  | Optical drive: | DVD-RW |  |
|  | Systems Management: | Full Remote Management (graphical console over LAN) Integrated Systems Management Processor; Systems Management SW included |  |
|  | High Availability Features: | Redundant hot-swap power supplies, fans Predicted Failure Analysis for critical components: HDD, power supplies, fans, memory, processor) |  |
|  | Security: | Trusted Platform Module (TPM) 1.2 Chip |  |
|  | Supported OS: | Windows, Linux, VMware |  |
|  | Warranty : | Three years onsite |  |
| Total Price, Item I |  |
| II | Storage System |  |  | 1 |  |
|  | Form-factor: | Rack-mountable | Offered Specification |
|  | Controller Type: | Dual-active Hot-Swap RAID controllers | Please, include detailed specification of offered equipment here. |
|  | Cache | 2GB; battery-backed; data dedicated |  |
|  | RAID Levels Supported | 0, 1, 10, 3, 5, 6 |  |
|  | Host Interface: | Four 8Gbps FC |  |
|  | Max. Capacity: | At least 100 HDDs |  |
|  | Drives installed: | Six 2TB 7.2K SATA hot-swap disks in RAID-6 Nine 450GB 4Gbps 15K FC hot-swap disks in RAID-5 plus one hot-spare disk |  |
|  | Availability Features | Switched backplane architecture Load balancing and Path failover feature to be included Redundant Power Supplies Cache destaging to flash drive |  |
|  | Partitioning | Min 4 storage partitions installed |  |
|  | Advanced Copy Features | Support for optional synchronous and asynchronous remote copy and instant local copy |  |
|  | OS Support | Support for Windows Server to be included; optional support for Linux, VMware, UNIX |  |
|  | Storage Management | Storage Management SW to be included |  |
|  | Warranty: | Three years onsite |  |
| Total Price, Item II |  |
| III. | SAN Switches |  |  | 2 |  |
|  | Form Factor: | Rack mount | Offered Specification |
|  | Total number of ports: | Twenty four | Please, include detailed specification of offered equipment here. |
|  | Enabled ports: | Eight ports; Eight 8Gbps SFPs; Support for 4Gbps speed |  |
|  | Management: | Web management tools |  |
|  | FC Cables: | Eight 5m LC-LC FC cables |  |
|  | Warranty: | One year onsite |  |
| Total Price, Item III |  |
| IV. | Backup server |  |  | 1 |  |
|  | Form Factor: | Rack mount; 1U; Sliding rails and cable management arm | Offered Specification |
|  | CPU: | One Intel Xeon Quad-Core Processor E5506 2.13GHz, expandable to two processors | Please, include detailed specification of offered equipment here. |
|  | RAM: | 12GB (3x4GB) DDR3 1333MHz RDIMM RAM; Advanced ECC; Eighteen memory slots max. |  |
|  | HDD: | Two 300GB 2.5”Hot-Swap 10K 6Gbps SAS; Eight disk bays |  |
|  | Internal RAID: | RAID 0, 1 |  |
|  | PCI Slots | One available PCI Express slot |  |
|  | Ports: | At least one front and one internal USB ports |  |
|  | Host Bus Adapters: | 8Gbps Dual-Port FC HBA Adapter |  |
|  | LAN: | Two independent Gigabit Ethernet ports with load balancing and failover |  |
|  | Optical drive: | DVD-RW |  |
|  | Systems Management: | Full Remote Management (graphical console over LAN) Integrated Systems Management Processor; Systems Management SW included |  |
|  | High Availability Features: | Redundant hot-swap power supplies, fans Predicted Failure Analysis for critical components: HDD, power supplies, fans, memory, processor) |  |
|  | Security: | Trusted Platform Module (TPM) 1.2 Chip |  |
|  | Supported OS: | Windows, Linux, VMware |  |
|  | Warranty : | Three years onsite |  |
| Total Price, Item IV |  |
| V. | Backup Device |  |  | 1 |  |
|  | Form Factor: | Rack mount | Offered Specification |
|  | Device Type: | LTO Tape Library | Please, include detailed specification of offered equipment here. |
|  | Host Interface: | 8Gbps Fibre Channel |  |
|  | Number of Drives: | Two LTO-5 |  |
|  | Max. Number of Tape Drives: | Four |  |
|  | Max. Tape Cartridge Capacity: | Forty eight |  |
|  | High Availability Features: | Path failover |  |
|  | Encryption | Support for optional transparent LTO encryption |  |
|  | Power Supplies | Dual redundant |  |
|  | Media: | Twenty five LTO-5 data cartridges, labeled; Two cleaning cartridges |  |
|  | OS Support | Native device driver support for Windows Server, Red Hat Linux and UNIX |  |
|  | Storage Management | Bar-code reader Web-based remote management |  |
|  | Warranty: | Three years on-site |  |
| Total Price, Item V |  |
| VI. | Backup SW |  |  | 1 |  |
|  | Architecture: | To run on a backup server (Item IV), operating system: Windows 2008 Server Standard Backup device: LTO Library (Item V) Backup source systems: 8 Virtual (MS Hyper-V) Windows 2008 Servers Enterprise 2x SQL Servers, 1x Exchange Server, 1x Sharepoint Services running on two physical servers (Item I); | Offered Specification |
|  | Functionality: | Backup and recovery management Disk-to-tape, disk-to-disk, disk-to-disk-to-tape backups Integration with MS SQL Server, Exchange Server and Sharepoint Services for online backup Support for incremental backups Policies-based archiving Data retention tools Optional automatic tools for planning the disaster recovery | Please, include detailed specification of offered equipment here. |
|  | Security: | Online data encryption between client and Server Integration with LTO tape built-in encryption Data shredding functionality |  |
|  | SW Maintenance: | One year |  |
| Total Price, Item VI |  |
| VII. | Ethernet Switches |  |  | 2 |  |
|  | Form Factor: | Rack mount | Offered Specification |
|  | Powers Supplies | Dual redundant | Please, include detailed specification of offered equipment here. |
|  | Ports: | Forty eight Ethernet 1Gb R45 ports, including 4 dual-purpose (RJ45 or SFP), optional two 10Gb Ethernet ports |  |
|  | Switch fabric: | 136Gbps |  |
|  | Forward rate: | 101Mpps |  |
|  | Management: | Web Management GUI; CLI, SNMP up to v3; RMON |  |
|  | Functionality: | IEEE 802.1d (STP), 802.1w (RSTP), 802.1s (MSTP) Single Spanning Tree Protocol (SSTP), PVST/PVST+, and Topology Groups IEEE 802.1q (VLAN tagging) IEEE 802.1p (Class of Service Prioritization) IEEE 802.1ad (Link Aggregation Control Protocol) IEEE 802.1x (Port Security) IGMPv1/v2/v3, PIM-SM & MLDv1/v2 snooping Policy controlled MAC-based VLANs MAC Learning Disable Port-based Access Control Lists BPDU Guard, Root Guard MAC-Layer Filtering Port Mirroring Uni-Directional Link Detection (UDLD) Auto MDI/MDIX Dynamic Voice VLAN Assignment Jumbo Frames up to 10,240 bytes IGMP Snooping Port Loop Detection Routed Interfaces IPv4 Static Routes DHCP and Bootp Relay QoS Queue Management using Weighted Round Robin (WRR), Strict Priority (SP) Inbound rate limiting per port ACL-based inbound rate limiting and traffic policies Outbound rate limiting per port and per queue Broadcast, multicast and unknown unicast rate limiting |  |
|  | Optional features: | Support for optional Class 3 (15.4W) Power over Ethernet (PoE) for 48 ports, Upgradable to RIP v1/v2, OSPF v2, |  |
|  | Warranty: | One year onsite |  |
| Total Price, Item VII |  |
| VIII. | Rack Infrastructure |  |  | 1 |  |
|  | Rack: | Industry standard (EIA 310) 19” 42U Rack; Depth min. 1000mm; Perforated front and rear doors Min. 6 side compartments; Room for cable management | Offered Specification |
|  | Console: | 1U 17” TFT Rack Console; Keyboard with pointing device | Please, include detailed specification of offered equipment here. |
|  | Console Switch: | 8 host ports; 8 sets of cables |  |
|  | PDU: | Two PDUs: input C19, output 7x C13 each |  |
|  | Warranty: | Three years onsite |  |
| Total Price, Item VIII |  |
| IX. | UPS |  |  | 2 |  |
|  | Form Factor: | Rack mount | Offered Specification |
|  | Capacity: | 4500W/5000VA | Please, include detailed specification of offered equipment here. |
|  | Functionality: | Hot-swappable batteries; Support for optional additional batteries; Ethernet network management card; Temperature sensor |  |
|  | Management SW: | To be included |  |
|  | Power outlets: | Two C19, eight C13 |  |
|  | Warranty: | Three years onsite |  |
| Total Price, Item IX |  |
| X. | Intrusion Prevention System |  |  | 1 |  |
|  | Form Factor: | Rack mount | Offered Specification |
|  | Number of ports: | 6 x 1Gb Ethernet | Please, include detailed specification of offered equipment here. |
|  | High Availability: | Yes! Two appliance should be included |  |
|  | Features: | IPS Stateful firewall, Ipsec and WEB VPN, Antivirus, spyware detection Antispam filtering Web content filtering |  |
|  | Performance: | Max. Firewall + IPS throughput – 450Mbps |  |
|  | Warranty: | One year hardware, software and signature updates |  |
| Total Price, Item X |  |
| XI. | Endpoint Security Solution |  |  | 1 |  |
|  | Clients number | 300 | Offered Specification |
|  | Features: | Intruder Prevention, Personal firewall, Antivirus, spyware detection, Application control, Automatic updates, Centralized Management System Support for Windows XP, Vista, Windows 7 | Please, include detailed specification of offered equipment here. |
|  | Warranty: | One year software and signature updates |  |
| Total Price Item XI |  |
| XII. | Software licenses |  |  |  |  |
|  |  | Microsoft Windows Server Enterprise 2008 R2 Eng., Open License, with media-kit |  | 2 |  |
|  |  | Microsoft Windows Server Standard 2008 R2 Eng., Open License, with media-kit |  | 1 |  |
|  |  | Microsoft Windows Server CAL 2008, Open License |  | 295 |  |
|  |  | Microsoft SQL Server Standard Eng., License+Software Assurance Pk, 1 Processor (per CPU license), Open License, with media-kit |  | 2 |  |
|  |  | Microsoft Exchange Server 2010 Standard, Open License, with media-kit |  | 1 |  |
|  |  | Microsoft Exchange 2010 Standard CAL |  | 295 |  |
| Total Price, Item XII |  |
| GRAND TOTAL |  |

- *Unit price should be based on Incoterms used i.e. DDU Chisinau, Moldova

- Note: In case of discrepancy between unit price and total, the unit price shall prevail.

Signature of Bidder ………………………………………..