WinСмета2000

| Reconstruction of Street Lighting System in Ustia village, Dubasari district | Sample No.1 |
| --- | --- |
| (objective) |  |

LOCAL COST ESTIMATE No. 1

Street lighting.  001/2013-IS.4 (l=1590m)

| No. | Symbol of norms and Code of resources | Works and Expenses | U/M | Amount according to the project data | Estimate value, lei |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Per unit of measurement ———— including salary | Total ————— Including salary |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 1. Construction works |  |  |  |  |
|  |  | 1.1. Pillar of the existing anchorage end A0.38/0.38, with additions (1pc) |  |  |  |  |
| 1 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,060 |  |  |
| 2 | 335000434-1 | - Grounding conductor ЗП2 | m | 0,600 |  |  |
| 3 | 335000515 | - Branching tightening device ПC-1-1 | pc | 1,000 |  |  |
| 4 | 33-04-005-1 | - Mounting of traverses | pc | 1,000 |  |  |
| 5 | 201-9285-07 | - Traverse TН-29 | pc | 1,000 |  |  |
| 6 | 335000521-10 | - Straining clamp HP25-55 | pc | 2,000 |  |  |
| 7 | 335000521-22 | - Tension clamp K-OHM-1 | pc | 1,000 |  |  |
| 8 | 335000521-19 | - Connexion clamp СНА-Н (СНА-И) | pc | 1,000 |  |  |
| 9 | 335000521-9 | - Connexion clamp СФ16-120 | pc | 4,000 |  |  |
| 10 | 201-9266-11 | Steel bracelets X11 | pc | 1,000 |  |  |
|  |  |  | Total Pillar of the existing anchorage end A0.38/0.38, with additions (1 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.2. Existing intermediary pillar П0.38/0.38, with additions (37 pc) |  |  |  |  |
| 11 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 2,220 |  |  |
| 12 | 335000434-1 | -Grounding conductor ЗП2 | m | 22,200 |  |  |
| 13 | 335000515 | -Branching tightening device ПC-1-1 | pc | 37,000 |  |  |
| 14 | 33500519-01 | - Suspended hook КБ1 | pc | 37,000 |  |  |
| 15 | 335000521-18 | - Support clamps ПН-1 | pc | 37,000 |  |  |
| 16 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 74,000 |  |  |
| 17 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 37,000 |  |  |
|  |  |  | Total Existing intermediary pillar .38/0.38, with additions (37 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.3. Existing intermediary corner pillar УП0.38/0.38, with additions (1pc) |  |  |  |  |
| 18 | 33-04-015-1 | Installation of the grounding of the LEA supports and substations | 10 m | 0,060 |  |  |
| 19 | 335000434-1 | Grounding conductor ЗП2 | m | 0,600 |  |  |
| 20 | 335000515 | -Branching tightening device ПC-1-1 | pc | 1,000 |  |  |
| 21 | 3350519-01 | - Suspended console KБ3.1 | pc | 1,000 |  |  |
| 22 | 335000521-18 | - Support clamps ПН-1 | pc | 1,000 |  |  |
| 23 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 2,000 |  |  |
| 24 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 1,000 |  |  |
|  |  |  | Total Existing intermediary corner pillar УП0.38/0.38, with additions (1pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.4. Designed poles |  |  |  |  |
| 25 | TsA16B1 | Manual excavation of ground, in confined spaces, in trenches for grounding and cable | m3 | 3,000 |  |  |
| 26 | TsD18B | Compacted filling in trenches for buried cables of high voltage power lines, made with middle ground | m3 | 3,000 |  |  |
| 27 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 9,000 |  |  |
| 28 | 33-04-005-1 | - Mounting of traverses | pc | 18,000 |  |  |
| 29 | 201-9285-04 | - Traverse TН-9 | pc | 18,000 |  |  |
| 30 | 201-9266-10 | - Steel bracelets X10 | pc | 18,000 |  |  |
| 31 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 1,485 |  |  |
| 32 | 335000434-1 | - Grounding conductor ЗП2M | m | 14,850 |  |  |
| 33 | 110-9034 | Electrical insulator HC 18 A | pc | 36,000 |  |  |
| 34 | 500-9056 | -Plastic cap K5 | pc | 36,000 |  |  |
| 35 | 335000516 | Branching tightening device ПA-1 | pc | 9,000 |  |  |
| 36 | 3350502-01 | -Stud MSN 16/265 | pc | 9,000 |  |  |
| 37 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 9,000 |  |  |
| 38 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 9,000 |  |  |
| 39 | 335000515 | - Branching tightening device ПC-1-1 | pc | 18,000 |  |  |
| 40 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 9,000 |  |  |
| 41 | 33500514-05 | -Cable strap KR-1 | pc | 18,000 |  |  |
| 42 | 33-04-016-2 | Transport of constructions and materials of supports LEA 0,38-10 kV on main line: of supports made ​​of reinforced concrete with one leg | pc | 9,000 |  |  |
|  |  |  | Total Designed poles |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | Direct expenses | MDL. |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Construction works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 2. Installation works |  |  |  |  |
| 43 | RpEF24B | Removal of incandescent bulbs 20-2000 W or of bulbs with mercury vapours | pc | 10,000 |  |  |
| 44 | RpEO01A | Removal of support with one arm | pc | 10,000 |  |  |
| 45 | RpEF23B | Dismounting of lighting installations | pc | 10,000 |  |  |
| 46 | 33-04-040-1 | Dismounting of 3 conductors LEA 0,38 kV | pc | 16,000 |  |  |
| 47 | 33-04-040-2 | Dismounting of an additional conductor LEA 0,38 kV | pc | 16,000 |  |  |
| 48 | 08-03-572-5 | Record cabinet mounted on wall, BZUM | pc | 1,000 |  |  |
| 49 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 50 | 08-03-526-1 | -Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 1,000 |  |  |
| 51 | 08-01-066-1 | -Lightning arrester, voltage up to10 kV | set | 1,000 |  |  |
| 52 | 08-03-600-2 | -Counters mounted on a prepared support with three phases | pc | 1,000 |  |  |
| 53 | 08-03-573-4 | Suspended control cabinet (desktop), height, width and depth, mm, up to 600х600х350 | pc | 1,000 |  |  |
| 54 | 08-03-526-1 | -Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 1,000 |  |  |
| 55 | 08-03-530-4 | Magnetic starter of common purpose, separated, mounted on construction wall or column, electric current up to 40 A | pc | 2,000 |  |  |
| 56 | 08-01-080-1 | Measurement and protection device, number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 57 | 08-03-525-1 | Packet breaker or switch in steel coating, mounted on wall or column construction, number of clamps for connection of up to 9, current up to 25 A | pc | 1,000 |  |  |
| 58 | 08-01-081-1 | Control and signalling device (button, control key, electromagnetic lock, acoustic signal, signalling lamp), number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 59 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A (installed in PT-547Y) | pc | 1,000 |  |  |
| 60 | 33-04-008-3 | Suspension of isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 1,240 |  |  |
| 61 | 33-04-008-1 | Suspension of non-isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 1,400 |  |  |
| 62 | 08-02-401-1 | Cable, fixing with applied clamps, strips with installation of branch box, with 2-4 wires, wire section up to 16 mm2 | 100 m | 0,550 |  |  |
| 63 | 08-01-087-3 | Steel structures | t | 0,092 |  |  |
| 64 | 08-01-082-1 | Clamps in assortment: clamp without protective frame | 100 pc | 1,680 |  |  |
| 65 | 08-01-052-1 | Support insulator, tension of up to 10 kV, number of fixing points: 1 | pc | 36,000 |  |  |
| 66 | 08-02-363-1 | Metal consoles, special, welded on poles, for lighting installations, number of bulbs: 1 | pc | 34,000 |  |  |
| 67 | 08-02-369-2 | Lighting installation with fluorescent bulbs, installed outside the buildings | pc | 34,000 |  |  |
| 68 | 33-04-015-1 | Installation of the grounding of the LEA supports and substations | 10 m | 3,400 |  |  |
| 69 | 08-02-142-1 | Execution of the bed for one cable in trenches | 100 m | 0,050 |  |  |
| 70 | 08-02-141-1 | Cable of up to 35 kV in trenches made ​​without coatings, weight 1 m, up to: 1 kg | 100 m | 0,100 |  |  |
| 71 | 08-02-148-1 | Cable of up to 35 kV in installed pipes, blocs and boxes, weight 1 m up to: 1 kg | 100 m | 0,050 |  |  |
| 72 | 08-02-396-6 | Metal channel on walls and ceilings, length of 2.5 m | 100 m | 0,050 |  |  |
| 73 | 33500514-05 | - Cable strap KR-1 | pc | 10,000 |  |  |
| 74 | 08-02-152-1 | Steel cable structures: corner steel 50x50x5mm (20m) | t | 0,075 |  |  |
| 75 | 08-02-472-9 | Open grounding conductor, on supports of construction, of round steel, diameter of 10 mm | 100 m | 1,300 |  |  |
| 76 | 08-02-472-6 | Open grounding conductor, on supports of construction, of strip steel, section of 100 mm2 | 100 m | 0,250 |  |  |
| 77 | 3331011-3 | Electric wire AC 35 | m | 1 400,000 |  |  |
| 78 | 3332017-3 | ABБбШв 4х25mm2 cable | m | 10,000 |  |  |
| 79 | 3332017-5 | ABБбШв 5х25mm2 cable | m | 5,000 |  |  |
| 80 | 3332040-3 | СИП-2 3х25+1х35 cable | m | 1 315,000 |  |  |
| 81 | 3332023-2 | ВВГ 3х2.5mm2 cable | m | 55,000 |  |  |
| 82 | 3341015-01 | Lighting installation with 65W,IP65 PКУ fluorescent bulbs | pc | 34,000 |  |  |
| 83 | 33400201-7 | 220V, 65W compact fluorescent bulbs | pc | 34,000 |  |  |
| 84 | 33890162-1 | Wall console for lighting installations with one arm | pc | 34,000 |  |  |
| 85 | 335000434 | Grounding conductor ЗП1M | m | 34,000 |  |  |
| 86 | 201-9266-16 | Steel bracelets X16 | pc | 34,000 |  |  |
| 87 | 33371012-08 | Perforated channel for cables 40x100x2500 | m | 5,000 |  |  |
| 88 | 33371012-05 | Cover for cable channel, base 100 | m | 5,000 |  |  |
|  |  | Direct expenses | MDL. |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Mounting works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 3. Outfit |  |  |  |  |
| 89 | 555050-1 | Record panel BZUM-TF-01-63-09 | set | 1,000 |  |  |
| 90 | 555-100012-2 | -Breaker BH32/4/20 , 20A | pc | 1,000 |  |  |
| 91 | 5550243-10 | -Automate breaker with 3 poles, 16A, BA47-29/3/16B | pc | 1,000 |  |  |
| 92 | 130-10015 | - De-tensioners ОПС1 B 4Р, In=30kA,Un=400V,In=60kA (MOP10-4-B) | pc | 1,000 |  |  |
| 93 | 5550061-01 | - "ZMR 110 ACe" 5-60A 220/380V three phase meter | pc | 1,000 |  |  |
| 94 | 55500087-31 | ЩРн-36з-0 74 У2 IP54, 540x330x120 (ЩУНО) distribution cabinet | pc | 1,000 |  |  |
| 95 | 5550243-8 | -Automate breaker with 3 poles, 10A, BA47-29/3/10B | pc | 1,000 |  |  |
| 96 | 33700305-4 | -Contactor KMИ-10910, 9А, 230B/AC3 1HO | pc | 2,000 |  |  |
| 97 | 338000504 | - PЭК78/4 relay | pc | 1,000 |  |  |
| 98 | 338101-01 | - РЧ-522 time relay with 2 channels | pc | 1,000 |  |  |
| 99 | 33800040-05 | - ALCLR-22 switch | pc | 1,000 |  |  |
| 100 | 33800014-7 | - SB-7 control button with 1 pin | pc | 2,000 |  |  |
| 101 | 5550243-11 | - 20A, BA47-29/3/20B (installed in PT280UBA 18) automate breaker with 3 poles | pc | 1,000 |  |  |
|  |  | Direct expenses | MDL. |  |  |  |
|  |  | Storage costs | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Outfit |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |

|  | Total cost estimate: |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Including salary |  |  |  |  |

| Drafted by |  |
| --- | --- |
| (position, signature) |
| Verified by |  |
| (position, signature) |

WinСмета2000

| Rebuilding street lighting system situated in Ustia village, Dubasari district | Sample No.1 |
| --- | --- |
| (objective) |  |

LOCAL COST ESTIMATE No. 2

Street lighting.  001/2013-IS.5 (l=6370m)

| No. | Symbol of norms and Code of resources | Works and Expenses | U/M | Amount according to the project data | Estimate value, lei |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Per unit of measurement ———— including salary | Total ————— including salary |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 1. Construction works |  |  |  |  |
|  |  | 1.1. Pillar of the existing anchorage end A0.38/0.38, with additions (2pc) |  |  |  |  |
| 1 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,120 |  |  |
| 2 | 335000434-1 | - Grounding conductor ЗП2 | m | 1,200 |  |  |
| 3 | 335000515 | - Branching tightening device ПC-1-1 | pc | 2,000 |  |  |
| 4 | 33-04-005-1 | - Mounting of traverses | pc | 2,000 |  |  |
| 5 | 201-9285-07 | - Traverse TН-29 | pc | 2,000 |  |  |
| 6 | 335000521-10 | - Straining clamp HP25-55 | pc | 4,000 |  |  |
| 7 | 335000521-22 | - Tension clamp K-OHM-1 | pc | 2,000 |  |  |
| 8 | 335000521-19 | - Connexion clamp СНА-Н | pc | 2,000 |  |  |
| 9 | 335000521-9 | - Connexion clamp СФ16-120 | pc | 8,000 |  |  |
| 10 | 201-9266-11 | Steel bracelets X11 | pc | 2,000 |  |  |
|  |  |  | Total Pillar of the existing anchorage end A0.38/0.38, with additions (2 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.2. Existing intermediary pillar П0.38/0.38, with additions (121 pc) |  |  |  |  |
| 11 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 7,260 |  |  |
| 12 | 335000434-1 | -Grounding conductor ЗП2 | m | 72,600 |  |  |
| 13 | 335000515 | -Branching tightening device ПC-1-1 | pc | 121,000 |  |  |
| 14 | 33500519-01 | - Suspended hook КБ1 | pc | 121,000 |  |  |
| 15 | 335000521-18 | - Support clamps ПН-1 | pc | 121,000 |  |  |
| 16 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 242,000 |  |  |
| 17 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 121,000 |  |  |
|  |  |  | Total Existing intermediary pillar П0.38/0.38, with additions (121 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.3. Designed poles |  |  |  |  |
| 18 | TsA16B1 | Manual excavation of ground, in confined spaces, in trenches for grounding and cable | m3 | 3,000 |  |  |
| 19 | TsD18B | Compacted filling in trenches for buried cables of high voltage power lines, made with middle ground | m3 | 3,000 |  |  |
| 20 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 41,000 |  |  |
| 21 | 33-04-005-1 | - Mounting of traverses | pc | 82,000 |  |  |
| 22 | 201-9285-04 | - Traverse TН-9 | pc | 82,000 |  |  |
| 23 | 201-9266-10 | - Steel bracelets X10 | pc | 82,000 |  |  |
| 24 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 6,765 |  |  |
| 25 | 335000434-1 | - Grounding conductor ЗП2M | m | 67,650 |  |  |
| 26 | 110-9034 | Electrical insulator HC 18 A | pc | 164,000 |  |  |
| 27 | 500-9056 | -Plastic cap K5 | pc | 164,000 |  |  |
| 28 | 335000516 | Branching tightening device ПA-1 | pc | 41,000 |  |  |
| 29 | 3350502-01 | -Stud MSN 16/265 | pc | 41,000 |  |  |
| 30 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 41,000 |  |  |
| 31 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 41,000 |  |  |
| 32 | 335000515 | - Branching tightening device ПC-1-1 | pc | 82,000 |  |  |
| 33 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 41,000 |  |  |
| 34 | 33500514-05 | -Cable strap KR-1 | pc | 82,000 |  |  |
| 35 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 6,000 |  |  |
| 36 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,600 |  |  |
| 37 | 335000434 | Grounding conductor ЗП1M | m | 6,000 |  |  |
| 38 | 3350502-01 | - Stud MSN 16/265 | pc | 6,000 |  |  |
| 39 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 6,000 |  |  |
| 40 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 6,000 |  |  |
| 41 | 335000515 | - Branching tightening device ПC-1-1 | pc | 6,000 |  |  |
| 42 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 6,000 |  |  |
| 43 | 33500514-05 | -Cable strap KR-1 | pc | 12,000 |  |  |
| 44 | 33-04-016-2 | Transport of constructions and materials of supports LEA 0,38-10 kV on main line: of supports made ​​of reinforced concrete with one leg | pc | 47,000 |  |  |
|  |  |  | Total Designed poles |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | Direct expenses | MDL. |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Construction works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 2. Installation works |  |  |  |  |
| 45 | RpEF24B | Removal of incandescent bulbs 20-2000 W or of bulbs with mercury vapours | pc | 35,000 |  |  |
| 46 | RpEO01A | Removal of support with one arm | pc | 35,000 |  |  |
| 47 | RpEF23B | Dismounting of lighting installations | pc | 35,000 |  |  |
| 48 | 33-04-040-1 | Dismounting of 3 conductors LEA 0,38 kV | pc | 72,000 |  |  |
| 49 | 33-04-040-2 | Dismounting of an additional conductor LEA 0,38 kV | pc | 72,000 |  |  |
| 50 | 08-03-572-5 | Record cabinet mounted on wall, BZUM | pc | 1,000 |  |  |
| 51 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 52 | 08-03-526-1 | -Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 1,000 |  |  |
| 53 | 08-01-066-1 | -Lightning arrester, voltage up to10 kV | set | 1,000 |  |  |
| 54 | 08-03-600-2 | -Counters mounted on a prepared support with three phases | pc | 1,000 |  |  |
| 55 | 08-03-573-4 | Suspended control cabinet (desktop), height, width and depth, mm, up to 600х600х350 | pc | 1,000 |  |  |
| 56 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 57 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 5,000 |  |  |
| 58 | 08-03-530-4 | Magnetic starter of common purpose, separated, mounted on construction wall or column, electric current up to 40 A | pc | 10,000 |  |  |
| 59 | 08-01-080-1 | Measurement and protection device, number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 60 | 08-03-525-1 | Packet breaker or switch in steel coating, mounted on wall or column construction, number of clamps for connection of up to 9, current up to 25 A | pc | 1,000 |  |  |
| 61 | 08-01-081-1 | Control and signalling device (button, control key, electromagnetic lock, acoustic signal, signalling lamp), number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 62 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A (installed in PT-547Y) | pc | 1,000 |  |  |
| 63 | 33-04-008-3 | Suspension of isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 4,760 |  |  |
| 64 | 33-04-008-1 | Suspension of non-isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 6,440 |  |  |
| 65 | 08-02-401-1 | Cable, fixing with applied clamps, strips with installation of branch box, with 2-4 wires, wire section up to 16 mm2 | 100 m | 1,900 |  |  |
| 66 | 08-01-087-3 | Steel structures | t | 0,360 |  |  |
| 67 | 08-01-082-1 | Clamps in assortment: clamp without protective frame | 100 pc | 6,040 |  |  |
| 68 | 08-01-052-1 | Support insulator, tension of up to 10 kV, number of fixing points: 1 | pc | 164,000 |  |  |
| 69 | 08-02-363-1 | Metal consoles, special, welded on poles, for lighting installations, number of bulbs: 1 | pc | 124,000 |  |  |
| 70 | 08-02-369-2 | Lighting installation with fluorescent bulbs, installed outside the buildings | pc | 124,000 |  |  |
| 71 | 33-04-015-1 | Installation of the grounding of the LEA supports and substations | 10 m | 12,400 |  |  |
| 72 | 08-02-142-1 | Execution of the bed for one cable in trenches | 100 m | 0,050 |  |  |
| 73 | 08-02-141-1 | Cable of up to 35 kV in trenches made ​​without coatings, weight 1 m, up to: 1 kg | 100 m | 0,100 |  |  |
| 74 | 08-02-148-1 | Cable of up to 35 kV in installed pipes, blocs and boxes, weight 1 m up to: 1 kg | 100 m | 0,050 |  |  |
| 75 | 08-02-396-6 | Metal channel on walls and ceilings, length of 2.5 m | 100 m | 0,050 |  |  |
| 76 | 08-02-152-1 | Steel cable structures: corner steel 50x50x5mm (20m) | t | 0,075 |  |  |
| 77 | 08-02-472-9 | Open grounding conductor, on supports of construction, of round steel, diameter of 10 mm | 100 m | 5,600 |  |  |
| 78 | 08-02-472-6 | Open grounding conductor, on supports of construction, of strip steel, section of 100 mm2 | 100 m | 0,250 |  |  |
| 79 | 3331011-3 | Electric wire AC 35 | m | 450,000 |  |  |
| 80 | 3332017-3 | ABБбШв 4х25mm2 cable | m | 10,000 |  |  |
| 81 | 3332017-5 | ABБбШв 5х25mm2 cable | m | 5,000 |  |  |
| 82 | 3332040-3 | СИП-2 3х25+1х35 cable | m | 5 055,000 |  |  |
| 83 | 3332023-2 | ВВГ 3х2.5mm2 cable | m | 190,000 |  |  |
| 84 | 3341015-01 | Lighting installation with 65W,IP65 PКУ fluorescent bulbs | pc | 124,000 |  |  |
| 85 | 33400201-7 | 220V, 65W compact fluorescent bulbs | pc | 124,000 |  |  |
| 86 | 33890162-1 | Wall console for lighting installations with one arm | pc | 124,000 |  |  |
| 87 | 335000434 | Grounding conductor ЗП1M | m | 124,000 |  |  |
| 88 | 201-9266-16 | Steel bracelets X16 | pc | 124,000 |  |  |
| 89 | 33371012-08 | Perforated channel for cables 40x100x2500 | m | 5,000 |  |  |
| 90 | 33371012-05 | Cover for cable channel, base 100 | m | 5,000 |  |  |
|  |  | Direct expenses | MDL. |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Mounting works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 3. Outfit |  |  |  |  |
| 91 | 555050-1 | Record panel BZUM-TF-01-63-09 | set | 1,000 |  |  |
| 92 | 555-100012-2 | - BH32/4/25 , 25A breaker | pc | 1,000 |  |  |
| 93 | 5550243-11 | - Automate breaker with 3 poles, 20A, BA47-29/3/20B | pc | 1,000 |  |  |
| 94 | 130-10015 | - De-tensioners ОПС1 B 4Р, In=30kA,Un=400V,In=60kA (MOP10-4-B) | pc | 1,000 |  |  |
| 95 | 5550061-01 | - "ZMR 110 ACe" 5-60A 220/380V three phase meter | pc | 1,000 |  |  |
| 96 | 55500087-32 | ЩРн-48з-0 74 У2 IP54, 670x330x120 distribution cabinet | pc | 1,000 |  |  |
| 97 | 555-100011-1 | - BH32/3/20 , 20A breaker | pc | 1,000 |  |  |
| 98 | 5550243-8 | - Automate breaker with 3 poles, 10A, BA47-29/3/10B | pc | 5,000 |  |  |
| 99 | 33700305-4 | -Contactor KMИ-10910, 9А, 230B/AC3 1HO | pc | 10,000 |  |  |
| 100 | 338000504 | - PЭК78/4 relay | pc | 1,000 |  |  |
| 101 | 338101-01 | - РЧ-522 time relay with 2 channels | pc | 1,000 |  |  |
| 102 | 33800040-05 | - ALCLR-22 switch | pc | 1,000 |  |  |
| 103 | 33800014-7 | - SB-7 control button with 1 pin | pc | 2,000 |  |  |
| 104 | 5550243-11 | - 20A, BA47-29/3/20B (installed in PT543Y) automate breaker with 3 poles | pc | 1,000 |  |  |
|  |  | Direct expenses | MDL. |  |  |  |
|  |  | Storage costs | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Outfit |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |

|  | Total cost estimate: |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Including salary |  |  |  |  |

| Drafted by |  |
| --- | --- |
| (position, signature) |
| Verified by |  |
| (position, signature) |

WinСмета2000

| Rebuilding street lighting system situated in Ustia village, Dubasari district | Sample No.1 |
| --- | --- |
| (objective) |  |

LOCAL COST ESTIMATE No. 3

Street lighting.  001/2013-IS.6 (l=3615m)

| No. | Symbol of norms and Code of resources | Works and Expenses | U/M | Amount according to the project data | Estimate value, lei |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Per unit of measurement ———— including salary | Total ————— including salary |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 1. Construction works |  |  |  |  |
|  |  | 1.1. Pillar of the existing anchorage end A0.38/0.38, with additions (2 pc) |  |  |  |  |
| 1 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,120 |  |  |
| 2 | 335000434-1 | - Grounding conductor ЗП2 | m | 1,200 |  |  |
| 3 | 335000515 | - Branching tightening device ПC-1-1 | pc | 2,000 |  |  |
| 4 | 33-04-005-1 | - Mounting of traverses | pc | 2,000 |  |  |
| 5 | 201-9285-07 | - Traverse TН-29 | pc | 2,000 |  |  |
| 6 | 335000521-10 | - Straining clamp HP25-55 | pc | 4,000 |  |  |
| 7 | 335000521-22 | - Tension clamp K-OHM-1 | pc | 2,000 |  |  |
| 8 | 335000521-19 | - Connexion clamp СНА-Н (СНА-И) | pc | 2,000 |  |  |
| 9 | 335000521-9 | - Connexion clamp СФ16-120 | pc | 8,000 |  |  |
| 10 | 201-9266-11 | Steel bracelets X11 | pc | 2,000 |  |  |
|  |  |  | Total Pillar of the existing anchorage end A0.38/0.38, with additions (2 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.2. Existing intermediary pillar П10/0.38, with additions (2 pc) |  |  |  |  |
| 11 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 0,120 |  |  |
| 12 | 335000434-1 | -Grounding conductor ЗП2 | m | 1,200 |  |  |
| 13 | 335000515 | -Branching tightening device ПC-1-1 | pc | 2,000 |  |  |
| 14 | 33500519-01 | - Suspended hook КБ1 | pc | 2,000 |  |  |
| 15 | 335000521-18 | - Support clamps ПН-1 | pc | 2,000 |  |  |
| 16 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 4,000 |  |  |
| 17 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 2,000 |  |  |
|  |  |  | Total Existing intermediary pillar П10/0.38, with additions (2 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.3. Existing intermediary pillar УП0.38/0.38, with additions (3 pc) |  |  |  |  |
| 18 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 0,180 |  |  |
| 19 | 335000434-1 | -Grounding conductor ЗП2 | m | 1,800 |  |  |
| 20 | 335000515 | -Branching tightening device ПC-1-1 | pc | 3,000 |  |  |
| 21 | 3350519-01 | - Suspended hook KБ3.1 | pc | 3,000 |  |  |
| 22 | 335000521-18 | - Support clamps ПН-1 | pc | 3,000 |  |  |
| 23 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 6,000 |  |  |
| 24 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 3,000 |  |  |
|  |  |  | Total Existing intermediary pillar УП0.38/0.38, with additions (3 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.4. Existing intermediary pillar П0.38/0.38, with additions (68 pc) |  |  |  |  |
| 25 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 4,080 |  |  |
| 26 | 335000434-1 | -Grounding conductor ЗП2 | m | 40,800 |  |  |
| 27 | 335000515 | -Branching tightening device ПC-1-1 | pc | 68,000 |  |  |
| 28 | 33500519-01 | - Suspended hook КБ1 | pc | 68,000 |  |  |
| 29 | 335000521-18 | - Support clamps ПН-1 | pc | 68,000 |  |  |
| 30 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 136,000 |  |  |
| 31 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 68,000 |  |  |
|  |  |  | Total Existing intermediary pillar П0.38/0.38, with additions (68 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.5. Designed poles |  |  |  |  |
| 32 | TsA16B1 | Manual excavation of ground, in confined spaces, in trenches for grounding and cable | m3 | 3,000 |  |  |
| 33 | TsD18B | Compacted filling in trenches for buried cables of high voltage power lines, made with middle ground | m3 | 3,000 |  |  |
| 34 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 24,000 |  |  |
| 35 | 33-04-005-1 | - Mounting of traverses | pc | 48,000 |  |  |
| 36 | 201-9285-04 | - Traverse TН-9 | pc | 48,000 |  |  |
| 37 | 201-9266-10 | - Steel bracelets X10 | pc | 48,000 |  |  |
| 38 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 3,960 |  |  |
| 39 | 335000434-1 | - Grounding conductor ЗП2M | m | 39,600 |  |  |
| 40 | 110-9034 | Electrical insulator HC 18 A | pc | 96,000 |  |  |
| 41 | 500-9056 | - Plastic cap K6 | pc | 96,000 |  |  |
| 42 | 335000516 | Branching tightening device ПA-1 | pc | 24,000 |  |  |
| 43 | 3350502-01 | - Stud MSN 16/265 | pc | 24,000 |  |  |
| 44 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 24,000 |  |  |
| 45 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 24,000 |  |  |
| 46 | 335000515 | - Branching tightening device ПC-1-1 | pc | 48,000 |  |  |
| 47 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 24,000 |  |  |
| 48 | 33500514-05 | -Cable strap KR-1 | pc | 48,000 |  |  |
| 49 | 33-04-003-3 | Mounting УА0,38 poles made of LEA 0,38, 6-10 kV reinforced concrete with traverses and no additions, with one leg and no prop | pc | 1,000 |  |  |
| 50 | 3350415-1 | - МУ103 panel (pad) | pc | 1,000 |  |  |
| 51 | 3350415-2 | - МУ104 panel (pad) | pc | 2,000 |  |  |
| 52 | 201-92611-3 | - У4 Console | pc | 2,000 |  |  |
| 53 | 33-04-005-1 | - Mounting of traverses | pc | 1,000 |  |  |
| 54 | 201-928646 | - Traverse TM46 | pc | 1,000 |  |  |
| 55 | 201-9266-33 | Steel bracelets X32 | pc | 1,000 |  |  |
| 56 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,200 |  |  |
| 57 | 335000434-1 | - Grounding conductor ЗП2M | m | 2,000 |  |  |
| 58 | 201-92857 | Anchorage clamp PA 1500 | pc | 2,000 |  |  |
| 59 | 335000521-20 | - Clamp for ЗП1М ZP-2 | pc | 1,000 |  |  |
| 60 | 3350401-01 | - MJPT phase conductor connector | pc | 4,000 |  |  |
| 61 | 3350401-02 | - MJPT neuter conductor connector | pc | 1,000 |  |  |
| 62 | 335000515 | - Branching tightening device ПC-1-1ПC-1-1 | pc | 2,000 |  |  |
| 63 | 33500514-05 | - Cable strap KR-1 | pc | 2,000 |  |  |
| 64 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 1,000 |  |  |
| 65 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,100 |  |  |
| 66 | 335000434 | Grounding conductor ЗП1M | m | 1,000 |  |  |
| 67 | 3350502-01 | - Stud MSN 16/265 | pc | 1,000 |  |  |
| 68 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 1,000 |  |  |
| 69 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 1,000 |  |  |
| 70 | 335000515 | - Branching tightening device ПC-1-1 | pc | 1,000 |  |  |
| 71 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 1,000 |  |  |
| 72 | 33500514-05 | - Cable strap KR-1 | pc | 2,000 |  |  |
| 73 | 33-04-016-2 | Transport of constructions and materials of supports LEA 0,38-10 kV on main line: of supports made ​​of reinforced concrete with one leg | pc | 28,000 |  |  |
|  |  |  | Total Designed poles |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Construction works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 2. Installation works |  |  |  |  |
| 74 | RpEF24B | Removal of incandescent bulbs 20-2000 W or of bulbs with mercury vapours | pc | 24,000 |  |  |
| 75 | RpEO01A | Removal of support with one arm | pc | 24,000 |  |  |
| 76 | RpEF23B | Dismounting of lighting installations | pc | 24,000 |  |  |
| 77 | 33-04-040-1 | Dismounting of 3 conductors LEA 0,38 kV | pc | 39,000 |  |  |
| 78 | 33-04-040-2 | Dismounting of an additional conductor LEA 0,38 kV | pc | 39,000 |  |  |
| 79 | 08-03-572-5 | Record cabinet mounted on wall, BZUM | pc | 1,000 |  |  |
| 80 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 81 | 08-03-526-1 | -Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 1,000 |  |  |
| 82 | 08-01-066-1 | -Lightning arrester, voltage up to10 kV | set | 1,000 |  |  |
| 83 | 08-03-600-2 | -Counters mounted on a prepared support with three phases | pc | 1,000 |  |  |
| 84 | 08-03-573-4 | Suspended control cabinet (desktop), height, width and depth, mm, up to 600х600х350 | pc | 1,000 |  |  |
| 85 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 86 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 2,000 |  |  |
| 87 | 08-03-530-4 | Magnetic starter of common purpose, separated, mounted on construction wall or column, electric current up to 40 A | pc | 4,000 |  |  |
| 88 | 08-01-080-1 | Measurement and protection device, number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 89 | 08-03-525-1 | Packet breaker or switch in steel coating, mounted on wall or column construction, number of clamps for connection of up to 9, current up to 25 A | pc | 1,000 |  |  |
| 90 | 08-01-081-1 | Control and signalling device (button, control key, electromagnetic lock, acoustic signal, signalling lamp), number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 91 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A (installed in PT-547Y) | pc | 1,000 |  |  |
| 92 | 33-04-008-3 | Suspension of isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 2,480 |  |  |
| 93 | 33-04-008-1 | Suspension of non-isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 4,540 |  |  |
| 94 | 08-02-401-1 | Cable, fixing with applied clamps, strips with installation of branch box, with 2-4 wires, wire section up to 16 mm2 | 100 m | 1,100 |  |  |
| 95 | 08-01-087-3 | Steel structures | t | 0,092 |  |  |
| 96 | 08-01-082-1 | Clamps in assortment: clamp without protective frame | 100 pc | 3,700 |  |  |
| 97 | 08-01-052-1 | Support insulator, tension of up to 10 kV, number of fixing points: 1 | pc | 96,000 |  |  |
| 98 | 08-02-363-1 | Metal consoles, special, welded on poles, for lighting installations, number of bulbs: 1 | pc | 71,000 |  |  |
| 99 | 08-02-369-2 | Lighting installation with fluorescent bulbs, installed outside the buildings | pc | 71,000 |  |  |
| 100 | 33-04-015-1 | Installation of the grounding of the LEA supports and substations | 10 m | 7,100 |  |  |
| 101 | 08-02-142-1 | Execution of the bed for one cable in trenches | 100 m | 0,050 |  |  |
| 102 | 08-02-141-1 | Cable of up to 35 kV in trenches made ​​without coatings, weight 1 m, up to: 1 kg | 100 m | 0,100 |  |  |
| 103 | 08-02-148-1 | Cable of up to 35 kV in installed pipes, blocs and boxes, weight 1 m up to: 1 kg | 100 m | 0,050 |  |  |
| 104 | 08-02-396-6 | Metal channel on walls and ceilings, length of 2.5 m | 100 m | 0,050 |  |  |
| 105 | 08-02-152-1 | Steel cable structures: corner steel 50x50x5mm (20m) | t | 0,075 |  |  |
| 106 | 08-02-472-9 | Open grounding conductor, on supports of construction, of round steel, diameter of 10 mm | 100 m | 2,500 |  |  |
| 107 | 08-02-472-6 | Open grounding conductor, on supports of construction, of strip steel, section of 100 mm2 | 100 m | 0,250 |  |  |
| 108 | 3331011-3 | Electric wire AC 35 | m | 300,000 |  |  |
| 109 | 3332017-3 | ABБбШв 4х25mm2 cable | m | 10,000 |  |  |
| 110 | 3332017-5 | ABБбШв 5х25mm2 cable | m | 5,000 |  |  |
| 111 | 3332040-3 | СИП-2 3х25+1х35 cable | m | 2 630,000 |  |  |
| 112 | 3332023-2 | ВВГ 3х2.5mm2 cable | m | 110,000 |  |  |
| 113 | 3341015-01 | Lighting installation with 65W,IP65 PКУ fluorescent bulbs | pc | 71,000 |  |  |
| 114 | 33400201-7 | 220V, 65W compact fluorescent bulbs | pc | 71,000 |  |  |
| 115 | 33890162-1 | Wall console for lighting installations with one arm | pc | 71,000 |  |  |
| 116 | 335000434 | Grounding conductor ЗП1M | m | 71,000 |  |  |
| 117 | 201-9266-16 | Steel bracelets X16 | pc | 71,000 |  |  |
| 118 | 33371012-08 | Perforated channel for cables 40x100x2500 | m | 5,000 |  |  |
| 119 | 33371012-05 | Cover for cable channel, base 100 | m | 5,000 |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Mounting works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 3. Outfit |  |  |  |  |
| 120 | 555050-1 | Record panel BZUM-TF-01-63-09 | set | 1,000 |  |  |
| 121 | 555-100012-2 | - BH32/4/20 , 20A breaker | pc | 1,000 |  |  |
| 122 | 5550243-10 | - 16A, BA47-29/3/16B automate breaker with 3 poles | pc | 1,000 |  |  |
| 123 | 130-10015 | - De-tensioners ОПС1 B 4Р, In=30kA,Un=400V,In=60kA (MOP10-4-B) | pc | 1,000 |  |  |
| 124 | 5550061-01 | - "ZMR 110 ACe" 5-60A 220/380V three phase meter | pc | 1,000 |  |  |
| 125 | 55500087-31 | ЩРн-36з-0 74 У2 IP54, 540x330x120 distribution cabinet | pc | 1,000 |  |  |
| 126 | 555-100011-1 | - BH32/3/20, 20A breaker | pc | 1,000 |  |  |
| 127 | 5550243-8 | - 10A, BA47-29/3/10B automate breaker with 3 poles | pc | 2,000 |  |  |
| 128 | 33700305-4 | - KMИ-10910, 9А, 230B/AC3 1HO Contactor | pc | 4,000 |  |  |
| 129 | 338000504 | - PЭК78/4 relay | pc | 1,000 |  |  |
| 130 | 338101-01 | - РЧ-522 time relay with 2 channels | pc | 1,000 |  |  |
| 131 | 33800040-05 | - ALCLR-22 switch | pc | 1,000 |  |  |
| 132 | 33800014-7 | - SB-7 control button with 1 pin | pc | 2,000 |  |  |
| 133 | 5550243-11 | - 20A, BA47-29/3/20B (installed in PT547Y) automate breaker with 3 poles | pc | 1,000 |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Storage costs | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Outfit |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |

|  | Total cost estimate: |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Including salary |  |  |  |  |

| Drafted by |  |
| --- | --- |
| (position, signature) |
| Verified by |  |
| (position, signature) |

WinСмета2000

| Rebuilding street lighting system situated in Ustia village, Dubasari district | Sample No.1 |
| --- | --- |
| (objective) |  |

LOCAL COST ESTIMATE No. 4

Street lighting.  001/2013-IS.7 (l=1245m)

| No. | Symbol of norms and Code of resources | Works and Expenses | U/M | Amount according to the project data | Estimate value, lei |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Per unit of measurement ———— including salary | Total ————— including salary |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 1. Construction works |  |  |  |  |
|  |  | 1.1. Pillar of the existing anchorage end A0.38/0.38, with additions (1 pc) |  |  |  |  |
| 1 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,060 |  |  |
| 2 | 335000434-1 | - Grounding conductor ЗП2 | m | 0,600 |  |  |
| 3 | 335000515 | - Branching tightening device ПC-1-1 | pc | 1,000 |  |  |
| 4 | 33-04-005-1 | - Mounting of traverses | pc | 1,000 |  |  |
| 5 | 201-9285-07 | - Traverse TН-29 | pc | 1,000 |  |  |
| 6 | 335000521-10 | - Straining clamp HP25-55 | pc | 2,000 |  |  |
| 7 | 335000521-22 | - Tension clamp K-OHM-1 | pc | 1,000 |  |  |
| 8 | 335000521-19 | - Connexion clamp СНА-Н (СНА-И) | pc | 1,000 |  |  |
| 9 | 335000521-9 | - Connexion clamp СФ16-120 | pc | 4,000 |  |  |
| 10 | 201-9266-11 | Steel bracelets X11 | pc | 1,000 |  |  |
|  |  |  | Total Pillar of the existing anchorage end A0.38/0.38, with additions (1pc ) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.2. Existing intermediary pillar УП0.38/0.38, with additions (2 pc) |  |  |  |  |
| 11 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 0,120 |  |  |
| 12 | 335000434-1 | -Grounding conductor ЗП2 | m | 1,200 |  |  |
| 13 | 335000515 | -Branching tightening device ПC-1-1 | pc | 2,000 |  |  |
| 14 | 3350519-01 | - Suspended hook KБ3.1 | pc | 2,000 |  |  |
| 15 | 335000521-18 | - Support clamps ПН-1 | pc | 2,000 |  |  |
| 16 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 4,000 |  |  |
| 17 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 2,000 |  |  |
|  |  |  | Total Existing intermediary pillar УП0.38/0.38, with additions (2 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.3. Existing intermediary pillar П0.38/0.38, with additions (31pc ) |  |  |  |  |
| 18 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 1,860 |  |  |
| 19 | 335000434-1 | -Grounding conductor ЗП2 | m | 18,600 |  |  |
| 20 | 335000515 | -Branching tightening device ПC-1-1 | pc | 31,000 |  |  |
| 21 | 33500519-01 | - Suspended hook КБ1 | pc | 31,000 |  |  |
| 22 | 335000521-18 | - Support clamps ПН-1 | pc | 31,000 |  |  |
| 23 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 62,000 |  |  |
| 24 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 31,000 |  |  |
|  |  |  | Total Existing intermediary pillar П0.38/0.38, with additions (31pc ) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.4. Designed poles |  |  |  |  |
| 25 | TsA16B1 | Manual excavation of ground, in confined spaces, in trenches for grounding and cable | m3 | 3,000 |  |  |
| 26 | TsD18B | Compacted filling in trenches for buried cables of high voltage power lines, made with middle ground | m3 | 3,000 |  |  |
| 27 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 7,000 |  |  |
| 28 | 33-04-005-1 | - Mounting of traverses | pc | 14,000 |  |  |
| 29 | 201-9285-04 | - Traverse TН-9 | pc | 14,000 |  |  |
| 30 | 201-9266-10 | - Steel bracelets X10 | pc | 14,000 |  |  |
| 31 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 1,155 |  |  |
| 32 | 335000434-1 | - Grounding conductor ЗП2M | m | 11,550 |  |  |
| 33 | 110-9034 | Electrical insulator HC 18 A | pc | 28,000 |  |  |
| 34 | 500-9056 | - Plastic cap K5 | pc | 28,000 |  |  |
| 35 | 335000516 | Branching tightening device ПA-1 | pc | 7,000 |  |  |
| 36 | 3350502-01 | - Stud MSN 16/265 | pc | 7,000 |  |  |
| 37 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 7,000 |  |  |
| 38 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 7,000 |  |  |
| 39 | 335000515 | - Branching tightening device ПC-1-1 | pc | 14,000 |  |  |
| 40 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 7,000 |  |  |
| 41 | 33500514-05 | -Cable strap KR-1 | pc | 14,000 |  |  |
| 42 | 33-04-016-2 | Transport of constructions and materials of supports LEA 0,38-10 kV on main line: of supports made ​​of reinforced concrete with one leg | pc | 7,000 |  |  |
|  |  |  | Total Designed poles |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Construction works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 2. Installation works |  |  |  |  |
| 43 | RpEF24B | Removal of incandescent bulbs 20-2000 W or of bulbs with mercury vapours | pc | 2,000 |  |  |
| 44 | RpEO01A | Removal of support with one arm | pc | 2,000 |  |  |
| 45 | RpEF23B | Dismounting of lighting installations | pc | 2,000 |  |  |
| 46 | 33-04-040-1 | Dismounting of 3 conductors LEA 0,38 kV | pc | 11,000 |  |  |
| 47 | 33-04-040-2 | Dismounting of an additional conductor LEA 0,38 kV | pc | 11,000 |  |  |
| 48 | 08-03-572-5 | Record cabinet mounted on wall, BZUM | pc | 1,000 |  |  |
| 49 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 50 | 08-03-526-1 | -Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 1,000 |  |  |
| 51 | 08-01-066-1 | -Lightning arrester, voltage up to10 kV | set | 1,000 |  |  |
| 52 | 08-03-600-2 | -Counters mounted on a prepared support with three phases | pc | 1,000 |  |  |
| 53 | 08-03-573-4 | Suspended control cabinet (desktop), height, width and depth, mm, up to 600х600х350 | pc | 1,000 |  |  |
| 54 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 1,000 |  |  |
| 55 | 08-03-530-4 | Magnetic starter of common purpose, separated, mounted on construction wall or column, electric current up to 40 A | pc | 2,000 |  |  |
| 56 | 08-01-080-1 | Measurement and protection device, number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 57 | 08-03-525-1 | Packet breaker or switch in steel coating, mounted on wall or column construction, number of clamps for connection of up to 9, current up to 25 A | pc | 1,000 |  |  |
| 58 | 08-01-081-1 | Control and signalling device (button, control key, electromagnetic lock, acoustic signal, signalling lamp), number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 59 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A (installed in PT555Y) | pc | 1,000 |  |  |
| 60 | 33-04-008-3 | Suspension of isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 0,980 |  |  |
| 61 | 33-04-008-1 | Suspension of non-isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 1,060 |  |  |
| 62 | 08-02-401-1 | Cable, fixing with applied clamps, strips with installation of branch box, with 2-4 wires, wire section up to 16 mm2 | 100 m | 0,400 |  |  |
| 63 | 08-01-087-3 | Steel structures | t | 0,050 |  |  |
| 64 | 08-01-082-1 | Clamps in assortment: clamp without protective frame | 100 pc | 1,430 |  |  |
| 65 | 08-01-052-1 | Support insulator, tension of up to 10 kV, number of fixing points: 1 | pc | 28,000 |  |  |
| 66 | 08-02-363-1 | Metal consoles, special, welded on poles, for lighting installations, number of bulbs: 1 | pc | 26,000 |  |  |
| 67 | 08-02-369-2 | Lighting installation with fluorescent bulbs, installed outside the buildings | pc | 26,000 |  |  |
| 68 | 33-04-015-1 | Installation of the grounding of the LEA supports and substations | 10 m | 2,600 |  |  |
| 69 | 08-02-142-1 | Execution of the bed for one cable in trenches | 100 m | 0,050 |  |  |
| 70 | 08-02-141-1 | Cable of up to 35 kV in trenches made ​​without coatings, weight 1 m, up to: 1 kg | 100 m | 0,100 |  |  |
| 71 | 08-02-148-1 | Cable of up to 35 kV in installed pipes, blocs and boxes, weight 1 m up to: 1 kg | 100 m | 0,050 |  |  |
| 72 | 08-02-396-6 | Metal channel on walls and ceilings, length of 2.5 m | 100 m | 0,050 |  |  |
| 73 | 08-02-152-1 | Steel cable structures: corner steel 50x50x5mm (20m) | t | 0,075 |  |  |
| 74 | 08-02-472-9 | Open grounding conductor, on supports of construction, of round steel, diameter of 10 mm | 100 m | 1,200 |  |  |
| 75 | 08-02-472-6 | Open grounding conductor, on supports of construction, of strip steel, section of 100 mm2 | 100 m | 0,250 |  |  |
| 76 | 3331011-3 | Electric wire AC 35 | m | 100,000 |  |  |
| 77 | 3332017-3 | ABБбШв 4х25mm2 cable | m | 10,000 |  |  |
| 78 | 3332017-5 | ABБбШв 5х25mm2 cable | m | 5,000 |  |  |
| 79 | 3332040-3 | СИП-2 3х25+1х35 cable | m | 1 040,000 |  |  |
| 80 | 3332023-2 | ВВГ 3х2.5mm2 cable | m | 40,000 |  |  |
| 81 | 3341015-01 | Lighting installation with 65W,IP65 PКУ fluorescent bulbs | pc | 26,000 |  |  |
| 82 | 33400201-7 | 220V, 65W compact fluorescent bulbs | pc | 26,000 |  |  |
| 83 | 33890162-1 | Wall console for lighting installations with one arm | pc | 26,000 |  |  |
| 84 | 335000434 | Grounding conductor ЗП1M | m | 26,000 |  |  |
| 85 | 201-9266-16 | Steel bracelets X16 | pc | 26,000 |  |  |
| 86 | 33371012-08 | Perforated channel for cables 40x100x2500 | m | 5,000 |  |  |
| 87 | 33371012-05 | Cover for cable channel, base 100 | m | 5,000 |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Mounting works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 3. Outfit |  |  |  |  |
| 88 | 555050-1 | Record panel BZUM-TF-01-63-09 | set | 1,000 |  |  |
| 89 | 555-100012-2 | - BH32/4/20 , 20A breaker | pc | 1,000 |  |  |
| 90 | 5550243-10 | - 16A, BA47-29/3/16B automate breaker with 3 poles | pc | 1,000 |  |  |
| 91 | 130-10015 | - De-tensioners ОПС1 B 4Р, In=30kA,Un=400V,In=60kA (MOP10-4-B) | pc | 1,000 |  |  |
| 92 | 5550061-01 | - "ZMR 110 ACe" 5-60A 220/380V three phase meter | pc | 1,000 |  |  |
| 93 | 55500087-32 | ЩРн-48з-0 74 У2 IP54, 670x330x120 distribution cabinet | pc | 1,000 |  |  |
| 94 | 5550243-8 | - 10A, BA47-29/3/10B automate breaker with 3 poles | pc | 1,000 |  |  |
| 95 | 33700305-4 | - KMИ-10910, 9А, 230B/AC3 1HO Contactor | pc | 2,000 |  |  |
| 96 | 338000504 | - PЭК78/4 relay | pc | 1,000 |  |  |
| 97 | 338101-01 | - РЧ-522 time relay with 2 channels | pc | 1,000 |  |  |
| 98 | 33800040-05 | - ALCLR-22 switch | pc | 1,000 |  |  |
| 99 | 33800014-7 | - SB-7 control button with 1 pin | pc | 2,000 |  |  |
| 100 | 5550243-11 | - 20A, BA47-29/3/20B (installed in PT555Y) automate breaker with 3 poles | pc | 1,000 |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Storage costs | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Outfit |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |

|  | Total cost estimate: |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Including salary |  |  |  |  |

| Drafted by |  |
| --- | --- |
| (position, signature) |
| Verified by |  |
| (position, signature) |

WinСмета2000

| Rebuilding street lighting system situated in Ustia village, Dubasari district | Sample No.1 |
| --- | --- |
| (objective) |  |

LOCAL COST ESTIMATE No. 6

Street lighting.  001/2013-IS.9 (l=4395m)

| No. | Symbol of norms and Code of resources | Works and Expenses | U/M | Amount according to the project data | Estimate value, lei |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Per unit of measurement ———— including salary | Total ————— including salary |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 1. Construction works |  |  |  |  |
|  |  | 1.1. Pillar of the existing anchorage end A0.38/0.38, with additions (1 pc) |  |  |  |  |
| 1 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,060 |  |  |
| 2 | 335000434-1 | - Grounding conductor ЗП2 | m | 0,600 |  |  |
| 3 | 335000515 | - Branching tightening device ПC-1-1 | pc | 1,000 |  |  |
| 4 | 33-04-005-1 | - Mounting of traverses | pc | 1,000 |  |  |
| 5 | 201-9285-07 | - Traverse TН-29 | pc | 1,000 |  |  |
| 6 | 335000521-10 | - Straining clamp HP25-55 | pc | 2,000 |  |  |
| 7 | 335000521-22 | - Tension clamp K-OHM-1 | pc | 1,000 |  |  |
| 8 | 335000521-19 | - Connexion clamp СНА-Н (СНА-И) | pc | 1,000 |  |  |
| 9 | 335000521-9 | - Connexion clamp СФ16-120 | pc | 4,000 |  |  |
| 10 | 201-9266-11 | Steel bracelets X11 | pc | 1,000 |  |  |
|  |  |  | Total Pillar of the existing anchorage end A0.38/0.38, with additions (1pc ) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.2. Existing intermediary pillar УП0.38/0.38, with additions (6pc ) |  |  |  |  |
| 11 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 0,360 |  |  |
| 12 | 335000434-1 | -Grounding conductor ЗП2 | m | 3,600 |  |  |
| 13 | 335000515 | -Branching tightening device ПC-1-1 | pc | 6,000 |  |  |
| 14 | 3350519-01 | - Suspended hook KБ3.1 | pc | 6,000 |  |  |
| 15 | 335000521-18 | - Support clamps ПН-1 | pc | 6,000 |  |  |
| 16 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 12,000 |  |  |
| 17 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 6,000 |  |  |
|  |  |  | Total Existing intermediary pillar УП0.38/0.38, with additions (6pc ) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.3. Existing intermediary pillar П0.38/0.38, with additions (82pc ) |  |  |  |  |
| 18 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 4,920 |  |  |
| 19 | 335000434-1 | -Grounding conductor ЗП2 | m | 49,200 |  |  |
| 20 | 335000515 | -Branching tightening device ПC-1-1 | pc | 82,000 |  |  |
| 21 | 33500519-01 | - Suspended hook КБ1 | pc | 82,000 |  |  |
| 22 | 335000521-18 | - Support clamps ПН-1 | pc | 82,000 |  |  |
| 23 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 164,000 |  |  |
| 24 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 2,000 |  |  |
|  |  |  | Total Existing intermediary pillar П0.38/0.38, with additions (82pc ) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.4. Existing intermediary pillar П10/0.38, with additions (16 pc ) |  |  |  |  |
| 25 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 0,960 |  |  |
| 26 | 335000434-1 | -Grounding conductor ЗП2 | m | 9,600 |  |  |
| 27 | 335000515 | -Branching tightening device ПC-1-1 | pc | 16,000 |  |  |
| 28 | 33500519-01 | - Suspended hook КБ1 | pc | 16,000 |  |  |
| 29 | 335000521-18 | - Support clamps ПН-1 | pc | 16,000 |  |  |
| 30 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 32,000 |  |  |
| 31 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 16,000 |  |  |
|  |  |  | Total Existing intermediary pillar П10/0.38, with additions (16pc ) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.5. Existing intermediary pillar УП10/0.38, with additions (6 pc) |  |  |  |  |
| 32 | 33-04-015-1 | -Installation of the grounding of the LEA supports and substations | 10 m | 0,360 |  |  |
| 33 | 335000434-1 | -Grounding conductor ЗП2 | m | 3,600 |  |  |
| 34 | 335000515 | -Branching tightening device ПC-1-1 | pc | 6,000 |  |  |
| 35 | 33500519-01 | - Suspended hook КБ1 | pc | 6,000 |  |  |
| 36 | 335000521-18 | - Support clamps ПН-1 | pc | 6,000 |  |  |
| 37 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 12,000 |  |  |
| 38 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 6,000 |  |  |
|  |  |  | Total Existing intermediary pillar УП10/0.38, with additions (6 pc) |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 1.6. Designed poles |  |  |  |  |
| 39 | TsA16B1 | Manual excavation of ground, in confined spaces, in trenches for grounding and cable | m3 | 3,000 |  |  |
| 40 | TsD18B | Compacted filling in trenches for buried cables of high voltage power lines, made with middle ground | m3 | 3,000 |  |  |
| 41 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 19,000 |  |  |
| 42 | 33-04-005-1 | - Mounting of traverses | pc | 38,000 |  |  |
| 43 | 201-9285-04 | - Traverse TН-9 | pc | 38,000 |  |  |
| 44 | 201-9266-10 | - Steel bracelets X10 | pc | 38,000 |  |  |
| 45 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 3,135 |  |  |
| 46 | 335000434-1 | - Grounding conductor ЗП2M | m | 31,350 |  |  |
| 47 | 110-9034 | Electrical insulator HC 18 A | pc | 76,000 |  |  |
| 48 | 500-9056 | - Plastic cap K5 | pc | 76,000 |  |  |
| 49 | 335000516 | Branching tightening device ПA-1 | pc | 19,000 |  |  |
| 50 | 3350502-01 | - Stud MSN 16/265 | pc | 19,000 |  |  |
| 51 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 19,000 |  |  |
| 52 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 19,000 |  |  |
| 53 | 335000515 | - Branching tightening device ПC-1-1 | pc | 38,000 |  |  |
| 54 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 19,000 |  |  |
| 55 | 33500514-05 | -Cable strap KR-1 | pc | 38,000 |  |  |
| 56 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 6,000 |  |  |
| 57 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,600 |  |  |
| 58 | 335000434 | Grounding conductor ЗП1M | m | 6,000 |  |  |
| 59 | 3350502-01 | - Stud MSN 16/265 | pc | 6,000 |  |  |
| 60 | 335000527-5 | -Console with intermediary clamp ES1500 | pc | 6,000 |  |  |
| 61 | 335000521-20 | -Clamp for ЗП1М ZP-2 | pc | 6,000 |  |  |
| 62 | 335000515 | - Branching tightening device ПC-1-1 | pc | 6,000 |  |  |
| 63 | 335000521-20 | - Clamp for ЗП2М KZP-2 | pc | 6,000 |  |  |
| 64 | 33500514-05 | - Cable strap KR-1 | pc | 12,000 |  |  |
| 65 | 33-04-003-1 | Mounting of intermediate poles П0.38/0.38 made of reinforced concrete with traverses and one leg | pc | 2,000 |  |  |
| 66 | 33-04-005-1 | - Mounting of traverses | pc | 2,000 |  |  |
| 67 | 201-92860 | Traverse TM1 (TM24) | pc | 2,000 |  |  |
| 68 | 201-9266-01 | Steel bracelets X1 | pc | 2,000 |  |  |
| 69 | 33-04-015-1 | - Installation of the grounding of the LEA supports and substations | 10 m | 0,120 |  |  |
| 70 | 335000434-1 | - Grounding conductor ЗП2M | m | 1,200 |  |  |
| 71 | 335000515 | - Branching tightening device ПC-1-1 | pc | 2,000 |  |  |
| 72 | 110-9030-1 | - Electrical insulator ШФ-20В | pc | 6,000 |  |  |
| 73 | 500-9058 | - Plastic cap K6 | pc | 6,000 |  |  |
| 74 | 33500521 | - Clamping electric conductors | pc | 6,000 |  |  |
| 75 | 335000522 | - Branching tightening device ПC-2 | pc | 2,000 |  |  |
| 76 | 33500519-01 | - Suspended hook КБ1 | pc | 2,000 |  |  |
| 77 | 335000521-18 | - Support clamps ПН-1 | pc | 2,000 |  |  |
| 78 | 201-92856 | - Steel bandage tape SOT 46 0.7x20x2000 | pc | 4,000 |  |  |
| 79 | 335000521-22 | - Branch clamp K-OHM-1 | pc | 2,000 |  |  |
| 80 | 33-04-016-2 | Transport of constructions and materials of supports LEA 0,38-10 kV on main line: of supports made ​​of reinforced concrete with one leg | pc | 27,000 |  |  |
|  |  |  | Designed poles |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Construction works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 2. Installation works |  |  |  |  |
| 81 | RpEF24B | Removal of incandescent bulbs 20-2000 W or of bulbs with mercury vapours | pc | 20,000 |  |  |
| 82 | RpEO01A | Removal of support with one arm | pc | 20,000 |  |  |
| 83 | RpEF23B | Dismounting of lighting installations | pc | 20,000 |  |  |
| 84 | 33-04-040-1 | Dismounting of 3 conductors LEA 0,38 kV | pc | 40,000 |  |  |
| 85 | 33-04-040-2 | Dismounting of an additional conductor LEA 0,38 kV | pc | 40,000 |  |  |
| 86 | 08-03-572-5 | Record cabinet mounted on wall, BZUM | pc | 1,000 |  |  |
| 87 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 88 | 08-03-526-1 | -Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 1,000 |  |  |
| 89 | 08-01-066-1 | -Lightning arrester, voltage up to10 kV | set | 1,000 |  |  |
| 90 | 08-03-600-2 | -Counters mounted on a prepared support with three phases | pc | 1,000 |  |  |
| 91 | 08-03-573-4 | Suspended control cabinet (desktop), height, width and depth, mm, up to 600х600х350 | pc | 1,000 |  |  |
| 92 | 08-03-521-15 | - Power circuit breaker | pc | 1,000 |  |  |
| 93 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A | pc | 2,000 |  |  |
| 94 | 08-03-530-4 | Magnetic starter of common purpose, separated, mounted on construction wall or column, electric current up to 40 A | pc | 4,000 |  |  |
| 95 | 08-01-080-1 | Measurement and protection device, number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 96 | 08-03-525-1 | Packet breaker or switch in steel coating, mounted on wall or column construction, number of clamps for connection of up to 9, current up to 25 A | pc | 1,000 |  |  |
| 97 | 08-01-081-1 | Control and signalling device (button, control key, electromagnetic lock, acoustic signal, signalling lamp), number of connected extremities up to: 2 | pc | 2,000 |  |  |
| 98 | 08-03-526-1 | - Mono-, bi-, three-pole automate device mounted on constructions, current up to 25 A (installed in PT538Y) | pc | 1,000 |  |  |
| 99 | 33-04-008-3 | Suspension of isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 3,440 |  |  |
| 100 | 33-04-008-1 | Suspension of non-isolated conductors by means of mechanisms LEA 0,38 kV | 1 km | 3,820 |  |  |
| 101 | 08-02-401-1 | Cable, fixing with applied clamps, strips with installation of branch box, with 2-4 wires, wire section up to 16 mm2 | 100 m | 1,400 |  |  |
| 102 | 08-01-087-3 | Steel structures | t | 0,200 |  |  |
| 103 | 08-01-082-1 | Clamps in assortment: clamp without protective frame | 100 pc | 4,600 |  |  |
| 104 | 08-01-052-1 | Support insulator, tension of up to 10 kV, number of fixing points: 1 | pc | 82,000 |  |  |
| 105 | 08-02-363-1 | Metal consoles, special, welded on poles, for lighting installations, number of bulbs: 1 | pc | 92,000 |  |  |
| 106 | 08-02-369-2 | Lighting installation with fluorescent bulbs, installed outside the buildings | pc | 92,000 |  |  |
| 107 | 33-04-015-1 | Installation of the grounding of the LEA supports and substations | 10 m | 9,200 |  |  |
| 108 | 08-02-142-1 | Execution of the bed for one cable in trenches | 100 m | 0,050 |  |  |
| 109 | 08-02-141-1 | Cable of up to 35 kV in trenches made ​​without coatings, weight 1 m, up to: 1 kg | 100 m | 0,100 |  |  |
| 110 | 08-02-148-1 | Cable of up to 35 kV in installed pipes, blocs and boxes, weight 1 m up to: 1 kg | 100 m | 0,050 |  |  |
| 111 | 08-02-396-6 | Metal channel on walls and ceilings, length of 2.5 m | 100 m | 0,050 |  |  |
| 112 | 08-02-152-1 | Steel cable structures: corner steel 50x50x5mm (20m) | t | 0,075 |  |  |
| 113 | 08-02-472-9 | Open grounding conductor, on supports of construction, of round steel, diameter of 10 mm | 100 m | 4,500 |  |  |
| 114 | 08-02-472-6 | Open grounding conductor, on supports of construction, of strip steel, section of 100 mm2 | 100 m | 0,250 |  |  |
| 115 | 3331011-3 | Electric wire AC 35 | m | 400,000 |  |  |
| 116 | 3332017-3 | ABБбШв 4х25mm2 cable | m | 10,000 |  |  |
| 117 | 3332017-5 | ABБбШв 5х25mm2 cable | m | 5,000 |  |  |
| 118 | 3332040-3 | СИП-2 3х25+1х35 cable | m | 3 650,000 |  |  |
| 119 | 3332023-2 | ВВГ 3х2.5mm2 cable | m | 140,000 |  |  |
| 120 | 3341015-01 | Lighting installation with 65W,IP65 PКУ fluorescent bulbs | pc | 92,000 |  |  |
| 121 | 33400201-7 | 220V, 65W compact fluorescent bulbs | pc | 92,000 |  |  |
| 122 | 33890162-1 | Wall console for lighting installations with one arm | pc | 92,000 |  |  |
| 123 | 335000434 | Grounding conductor ЗП1M | m | 92,000 |  |  |
| 124 | 201-9266-16 | Steel bracelets X16 | pc | 92,000 |  |  |
| 125 | 33371012-08 | Perforated channel for cables 40x100x2500 | m | 5,000 |  |  |
| 126 | 33371012-05 | Cover for cable channel, base 100 | m | 5,000 |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Social insurance fund | 26,50 % |  |  |  |
|  |  | Transport | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Overheads | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  | Benefit | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Mounting works |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |
|  |  | 3. Outfit |  |  |  |  |
| 127 | 555050-1 | Record panel BZUM-TF-01-63-09 | set | 1,000 |  |  |
| 128 | 555-100012-2 | - BH32/4/20 , 20A breaker | pc | 1,000 |  |  |
| 129 | 5550243-10 | - 16A, BA47-29/3/16B automate breaker with 3 poles | pc | 1,000 |  |  |
| 130 | 130-10015 | - De-tensioners ОПС1 B 4Р, In=30kA,Un=400V,In=60kA (MOP10-4-B) | pc | 1,000 |  |  |
| 131 | 5550061-01 | - "ZMR 110 ACe" 5-60A 220/380V three phase meter | pc | 1,000 |  |  |
| 132 | 55500087-31 | ЩРн-36з-0 74 У2 IP54, 540x330x120 distribution cabinet | pc | 1,000 |  |  |
| 133 | 555-100011-1 | - BH32/3/20, 20A breaker | pc | 1,000 |  |  |
| 134 | 5550243-8 | - 10A, BA47-29/3/10B automate breaker with 3 poles | pc | 2,000 |  |  |
| 135 | 33700305-4 | -Contactor KMИ-10910, 9А, 230B/AC3 1HO | pc | 4,000 |  |  |
| 136 | 338000504 | - PЭК78/4 relay | pc | 1,000 |  |  |
| 137 | 338101-01 | - РЧ-522 time relay with 2 channels | pc | 1,000 |  |  |
| 138 | 33800040-05 | - ALCLR-22 switch | pc | 1,000 |  |  |
| 139 | 33800014-7 | - SB-7 control button with 1 pin | pc | 2,000 |  |  |
| 140 | 5550243-11 | - 20A, BA47-29/3/20B (installed in PT547Y) automate breaker with 3 poles | pc | 1,000 |  |  |
|  |  | Direct expenses | lei |  |  |  |
|  |  | Storage costs | % |  |  |  |
|  |  | Total | + |  |  |  |
|  |  |  | Total Outfit |  |  |  |  |
|  |  |  | Including salary |  |  |  |  |

|  | Total cost estimate: |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Including salary |  |  |  |  |

| Drafted by |  |
| --- | --- |
| (position, signature) |
| Verified by |  |
| (position, signature) |