Annex 3

Technical responsiveness table

|  | Item | Minimum requirements/specifications | Yes/No (please provide details) |
| --- | --- | --- | --- |
|  | Item 1 Video and Audio Conferencing System and accessories |
| 1 | Video conferencing system | Similar to POLYCOM RealPresence Group 700 - with 2 full HD cameras and necessary software and accessories |  |
| 2 | Display | Size (inch) 80 Aspect Ratio 16:9 Resolution 1920x1080 Full HD USB 2.0 2 HDMI 2 Ethernet (LAN) 1 RCA 1 Component in (Y/Pb/Pr) + Audio 1 Color black Ceiling or wall mounting possibility Yes |  |
| 3 | Wall mount adjustable support bracket | Compatible with 80 inch display |  |
| 4 | Display | Screen size (inch) 48 Aspect Ratio 16:9 Resolution 1920x1080 Full HD USB 2.0 2 HDMI 2 Ethernet (LAN) 1 RCA 1 Component in (Y/Pb/Pr) + Audio 1 Color black Ceiling or wall mounting possibility yes |  |
| 5 | Ceiling mount adjustable support bracket | Compatible with 48 inch display |  |
| 6 | Wireless Audio Conference System | Wireless transmission technology Immunity to RF interference from mobile phones and comparable devices Sound quality: Freq. Response: 20 Hz ~ 20 kHz, S/N: >80 dBA Supply voltage: AC 210-240 V, 50-60 Hz Application software included USB interface Ethernet interface Video switcher interface LINE IN interface for connection to an external audio device Multiple discussion modes Multiple simultaneous interpretation Information LCD display Rack mount ready |  |
| 7 | Chairman unit | Wireless technology Microphone with flexible stem On/Off microphone button On/Off light indicator Channel selector Priority button Battery life (with mic On): min 8 hours Rechargeable battery pack Pluggable microphone Transmitting up to 64 CHs high quality digital audio Immunity to RF interference from mobile devices Built-in loudspeaker Built-in volume control for headphones 3.5 mm stereo headphone jack 3.5 mm socket for external microphone or headset microphone Frequency response 20 Hz to 20 kHz Tabletop mounted |  |
| 8 | Delegate unit | Wireless technology Microphone with flexible stem On/Off microphone button On/Off light indicator Channel selector Battery life (with mic On): min 8 hours Rechargeable battery pack Pluggable microphone Transmitting up to 64 CHs high quality digital audio Immunity to RF interference from mobile devices Built-in loudspeaker Built-in volume control for headphones 3.5 mm stereo headphone jack 3.5 mm socket for external microphone or headset microphone Frequency response 20 Hz to 20 kHz Tabletop mounted |  |
| 9 | Charging unit compatible with Chairman and Delegate units (positions 7 and 8) |  |
| 10 | Wireless Signal Transceiver | Ceiling, wall or tripod mounting, easy to install Signal range min 15 m from the unit Distribution of min 4 audio channels 3.5 mm stereo headphone socket LCD display Adjustable sensitivity Supply voltage: AC 210-240 V, 50-60 Hz |  |
| 11 | Wireless receiver | For four handheld wireless microphones Carrier frequency range 795 MHz – 820 MHz Frequency response 80 Hz - 15 kHz S/N ratio > 105 dB |  |
| 12 | Wireless microphones | Handheld wireless microphone transmitters On/Off button Immunity to RF interference from mobile devices Rechargeable battery Battery life (mic On): min 8 hours |  |
| 13 | Charging unit for 4 wireless microphones compatible with item 12 above |  |
| 14 | Speakers | Active ceiling loudspeaker 30W |  |
| 15 | Amplifier | Mixing amplifier for active loudspeakers, 240W |  |
| 16 | UPS | Output Power Capacity: 1000 Watts / 1500 VA Nominal Output Voltage: 230V Output Voltage Distortion: Less than 5% at full load Waveform Type: Sine wave Output Connections: (4) IEC 320 C13 Nominal Input Voltage: 230V Input Frequency: 50/60 Hz +/- 3 Hz (auto sensing) Input voltage adjustable range for mains operation: 151 - 302V Rack mount ready |  |
| 17 | Rack | Rack 18U for passive equipment with PDU with cooling system and min. 4 power sockets |  |
| 18 | Wireless interpretation and language distribution system | General Support min 60 persons Cover up to 400 m2 Supply voltage: AC 210-240 V, 50-60 Hz |  |
|  |  | Transmitter Mounting brackets Distribution of min 4 audio channels Signal range min 15 m from the unit Rack mount ready Adjustable sensitivity LCD display 3.5 mm stereo headphone socket |  |
|  |  | Simultaneous Interpretation Unit: Ready to use for two users Accommodate at least 2 languages Up to 64 channels Immunity to RF interference from mobile phones LCD display Built-in loudspeaker Volume control Microphone with flexible stem and On/Off light indicator Adjustable microphone sensitivity Repeat function Headphone volume control Microphone mute button 2 x 3.5 mm stereo jack for headphone 2 x high quality dynamic headphones for interpreters Tabletop mounting |  |
| 19 | Wireless Pocket Receiver With Stereo Headphones | On/Off button Rechargeable battery Battery life: up to 8 hours Volume control Min 4 audio channels LCD display |  |
| 20 | Storage case for the wireless pocket receivers | To store at least 60 receivers Reinforced corners Shaped foam padding |  |
| 21 | Charging unit for wireless receivers | For at least 50 receivers at one time On/Off switch |  |
| 22 | Cables, software and accessories for equipment installation, configuration and integration |  |
| 23 | Installation services and testing |  |
| 24 | Training for end users |  |
| 25 | Maintenance Services | 24 months |  |
| 26 | Expected delivery schedule – up to 35 calendar days Delivery of equipment to Moldova – up to 28 calendar days Installation, configuration and integration of equipment – up to 5 calendar days Testing of equipment – 1 calendar day Training of assigned staff – 1 calendar day |  |
| Item 2 Multimedia and audio system |
| 1 | Interactive whiteboard system | 87 inch screen Touch resolution: 4000 x 4000 or better Use a finger or pen to write on the interactive whiteboard and to control applications Allow up to four users to perform tasks simultaneously Low-gloss durable surface Dry erase compatible Audio connectivity Remote control Aspect ratio: 16:10 Supply voltage: AC 210-240 V, 50-60 Hz Compatible with Windows® operating system software Provided with dedicated software applications Wall mounting brackets Ultra short projector: minimum brightness: 3500 lumens resolution: WXGA 1280 × 800 video interface: HDMI (x2) and VGA (RGB or Component) audio interface: 3.5 mm phone jack audio input, 3.5 mm phone jack audio output minimum lamp life of 1500 hours, standard mode |  |
| 2 | Audio system | Audio signal splitter Minimum 4 mic/line out Wireless microphone signal receiver LCD display Signal range min 15 m from the unit Adjustable sensitivity Rack mount ready Supply voltage: AC 210-240 V, 50-60 Hz 3.5 mm stereo headphone socket |  |
| 3 | Wireless microphones | Handheld wireless microphone transmitters On/Off button Immunity to RF interference from mobile devices Rechargeable battery Battery life (mic On): min 8 hours |  |
| 4 | Charging unit for 4 wireless microphones compatible with position 3 above |  |
| 5 | Speakers | Active ceiling loudspeaker 30W |  |
| 6 | Amplifier | Mixing amplifier for active loudspeakers, 240W |  |
| 7 | UPS | Output Power Capacity: 1000 Watts / 1500 VA Nominal Output Voltage: 230V Output Voltage Distortion: Less than 5% at full load Waveform Type: Sine wave Output Connections: (4) IEC 320 C13 Nominal Input Voltage: 230V Input Frequency: 50/60 Hz +/- 3 Hz (auto sensing) Input voltage adjustable range for mains operation: 151 - 302V Rack mount ready |  |
| 8 | Rack | Rack 14U for passive equipment with PDU with cooling system and min. 4 power sockets |  |
| 9 | Cables, software and accessories for equipment installation, configuration and integration |  |
| 10 | Installation services and testing |  |
| 11 | Training for end users |  |
| 12 | Maintenance Services | 24 months |  |
| 13 | Expected delivery schedule – up to 35 calendar days Delivery of equipment to Moldova – up to 28 calendar days Installation, configuration and integration of equipment – up to 5 calendar days Testing of equipment – 1 calendar day Training of assigned staff – 1 calendar day |  |

All other information that we have not provided automatically implies our full compliance with the requirements, terms and conditions of the RFQ.

[Name and Signature of the Supplier’s Authorized Person]

[Designation]

[Date]