Annex 3

Technical responsiveness table

|  | Minimum requirements/specifications | Yes/No (please provide details) |
| --- | --- | --- |
| Item 1 | Ethernet Switch (Type 1) |  |
|  | Type: Gigabit Ethernet Ports: 24 x RJ-45 10/100/1000 ports; Duplex: 10BASE-T/100BASE-TX: half or full; 1000BASE-T: full only; 2 x SFP 100/1000 Mbps transceiver slots Management interface: yes Performance: Throughput – at least 20 million pps Switching capacity – at least 24 Gbps MAC address table – at least 4,000 entries Characteristics: Layer 2 switching: VLAN support and tagging IEEE 802.1Q, Resiliency and high availability: IEEE 802.1D Spanning Tree Protocol (STP) and IEEE 802.1W Rapid Spanning Tree Protocol (RSTP) Security Management: Secure Sockets Layer (SSL), Automatic denial-of-service protection, Management password Management: Simple/Secure management, SNMPv1, SNMPv2, Port mirroring |  |
|  | Rack mount ready (EIA-standard) |  |
|  | Voltage: 210-240 V AC |  |
|  | Warranty – 3 years |  |
| Item 2 | Ethernet Switch (Type 2) |  |
|  | Type: Gigabit Ethernet modular Ports: 48 x RJ-45 autosensing 10/100/1000 PoE+ ports; Media Type: Auto MDIX; Duplex: 10BASE-T/100BASE-TX: half or full; 1000BASE-T: full only 2 x 1Gb SFP transceiver slots Management interface: yes Performance: Throughput – 225 million pps Routing/switching capacity – at least 320 Gbps Switch fabric speed – at least 48 Gbps/slot Routing table – 10,000 entries MAC address table – at least 20,000 entries Characteristics: Supports OpenFlow Quality of Service (QoS): Advanced classifier-based QoS, Layer 4 prioritization, Traffic prioritization, Bandwidth shaping, Class of Service (CoS) Management: Remote intelligent mirroring, RMON, XRMON, sFlow v5, LLDP, UDLD, Friendly port names, Dual flash images, Multiple configuration files, CLI Connectivity: IEEE 802.3az, IEEE 802.3af, IEEE 802.3at, Prestandard PoE support, Jumbo frames, Auto-MDIX, IPv6 Resiliency and high availability: VRRP, Nonstop switching, Nonstop routing, Redundant management and power, IEEE 802.1s, IEEE 802.3ad, Distributed trunking, Hot-swappable modules, Uplink Failure Detection Layer 2 switching: VLAN support and tagging IEEE 802.1Q, IEEE 802.1v , GARP VLAN Registration Protocol, IEEE 802.1ad Q-in-Q, MAC-based VLAN, RPVST+ Layer 3 routing: Static IP routing, RIP, OSPF, Policy-based routing, BGP Security: Access control lists, Multiple user authentication methods, DHCP Relay, DHCP Server, DHCP Snooping, DHCP Security, Secure management access, Dynamic IP lockdown, Dynamic ARP protection, STP Root Guard, Port security, MAC address lockout, Source-port filtering Convergence: IP multicast routing, IP multicast snooping, LLDP-MED |  |
|  | Rack mount ready (EIA-standard) |  |
|  | Voltage: 210-240 V AC |  |
|  | Warranty – 3 years |  |
| Item 3 | Router/Firewall (Type 1) |  |
|  | Type: UTM security appliances Ports: 8 x GbE RJ45 Port 2 x SFP port Console port Internal memory: min 2Gb Performance: Firewall Throughput – at least 1.2Gbps for UDP packets Firewall Throughput (Packets Per Second) – at least 5 Mpps Concurrent sessions (TCP) – at least 250,000 New sessions/Sec (TCP) – at least 8,000 Firewall Policies – at least 5,000 IPSec VPN Throughput (512 byte packet) – at least 256 Mbps Site-to-Site IPSec VPN Tunnel – at least 200 Client-to-Site IPSec VPN Tunnels – at least 1,000 Number of licensed clients – at least 200 |  |
|  | Voltage: 210-240 V AC |  |
|  | Warranty – 3 years |  |
| Item 4 | Router/Firewall (Type 2) |  |
|  | Type: UTM security appliances Ports: 8 x GbE RJ45 port 4 x GbE SFP Port 1 x management interface Internal memory: min 20GB Processor: ASIC Performance: Firewall Throughput – at least 1.4 Gbps for UDP packets Firewall Throughput (Packets Per Second) – at least 24 Mpps Concurrent sessions (TCP) – at least 500,000 New session/Sec (TCP) – at least 50,000 Firewall Policies – at least 10,000 IPSec VPN Throughput (512 byte packet) – at least 1 Gbps Site-to-Site IPSec VPN Tunnel – at least 2,000 Client-to-Site IPSec VPN Tunnels – at least 5,000 SSL-VPN Throughput – at least 700 Mbps Concurrent user SSL-VPN – 5,000 IPS Throughput – at least 512 Mbps Unlimited number of clients High Availability supported configurations - Active / Active, Active / Passive, Clustering |  |
|  | Voltage: 210-240 V AC |  |
|  | Warranty – 3 years |  |
| Item 5 | 9U Rack |  |
| Item 6 | Patch panel 24 ports RJ-45 |  |
| Item 7 | Works and consumables for the installation of rack and equipment and configuration of installed devices in all 51 locations |  |