Annex 3

Technical responsiveness table

| Item | GENERIC SPECIFIATIONS | Yes/No (please provide details) |
| --- | --- | --- |
| 1. | Server (Type 1) |  |
|  | 1st CPU | 8-cores Processor, similar to Intel Xeon E5 v3, 3.0 GHz, 20MB cache |  |
|  | 2nd CPU | 8-cores Processor, similar to Intel Xeon E5 v3, 3.0 GHz, 20MB cache |  |
|  | RAM | 64 GB DDR4 |  |
|  | Hard Drive | 5 x 1.2 TB 6G SAS 10K rpm |  |
|  | RAID Controller | RAID 6 or dual parity capable, 2GB cache |  |
|  | LAN | Integrated, 4 x 1Gb |  |
|  | Optical drive | Optional |  |
|  | Management | Integrated out-of-band management with virtual media and remote KVM |  |
|  | Ports | 2 USB 2.0 front, 2 USB 2.0 rear, 1 serial interface |  |
|  | Slots | 2 x open slots PCIe 3.0 8x for expansion |  |
|  | Power Supply | 2 x hot plug power supplies, 500W Platinum efficiency |  |
|  | Form Factor | 1U, including rail kit |  |
|  | Warranty | 3 years from manufacturer, parts and labor included |  |

| Item | GENERIC SPECIFIATIONS | Yes/No (please provide details) |
| --- | --- | --- |
| 2. | Server (Type 2) |  |
|  | 1st CPU | 8-cores Processor, similar to Intel Xeon E5 v3, 3.0 GHz, 20MB cache |  |
|  | 2nd CPU | 8-cores Processor, similar to Intel Xeon E5 v3, 3.0 GHz, 20MB cache |  |
|  | RAM | 64 GB DDR4 |  |
|  | Hard Drive | 2 x 400 GB 6G SSD |  |
|  | RAID Controller | RAID 1, 2GB cache |  |
|  | LAN | Integrated, 4 x 1Gb |  |
|  | Optical drive | Optional |  |
|  | Management | Integrated out-of-band management with virtual media and remote KVM |  |
|  | Ports | 2 USB 2.0 front, 2 USB 2.0 rear, 1 serial interface |  |
|  | Slots | 2 x open slots PCIe 3.0 8x for expansion |  |
|  | Power Supply | 2 x hot plug power supplies, 500W Platinum efficiency |  |
|  | Form Factor | 1U, including rail kit |  |
|  | Warranty | 3 years from manufacturer, parts and labor included |  |

| Item | GENERIC SPECIFIATIONS | Yes/No (please provide details) |
| --- | --- | --- |
| 3. | UPS |  |
|  | Shall provide minimum 45 minutes autonomy for both servers |  |
|  | Form factor | 1U, including rail kit |  |