| Repairing works of the Polyclinics building in Dnestrovsc town | Form Nr.1 WinСmeta |
| --- | --- |
| (name of the site) |  |

LOCAL ESTIMATES № 1

Capital repairing works of the Polyclinics building in Dnestrovsc town

Concluded based on current prices

| № | Symbol of the norm and resource code | Works and expenses | U.M. | Quantity according to the design data | Estimate value, USD |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Per U.M ———— incl. salary | Total ————— incl. salary |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 1. General repairing works |  |  |  |  |
|  |  | 1.1. Roof |  |  |  |  |
| 1 | RpCI42B | Dismantling roof elements – asbestos-cement cover and afferent elements | m2 | 912,0000 |  |  |
| 2 | RpCH32B | Displacing the wood boards and the roof elements – framing of the roof, by undoing all the component elements, including the sorting of the resulted materials | m2 | 682,5000 |  |  |
| 3 | RpCH02A | Resinous wooden framing, on simple roofs, with one with up to 4 slopes, for covering from tiling, from square timber, for light roofs | m2 | 682,5000 |  |  |
| 4 | RpCH05E | Replacing the elements of damaged framing with new ones – resinous round wood stamps | m | 45,0000 |  |  |
| 5 | RpCH05B | Replacing the elements of damaged framing with new ones – resinous trusses | m | 78,0000 |  |  |
| 6 | RpCH05A | Replacing the elements of damaged framing with new ones - rafters by doubling between two supports of rulers | m | 90,0000 |  |  |
| 7 | RpCH07A1 | Repairing the revetment of the covering of resinous boards, of 24 mm width, executed via replacement of the broken revetment with boards for usual constructions, for total replacement of the revetment | m2 | 912,0000 |  |  |
| 8 | CE07A | Covering from imprinted board plates (roof tile) for covering the roofs (Lindab type) Metallic tiles of "Monterrey" type, thickness 0.5 mm (board norm =1.22m2) or equivalent | m2 | 912,0000 |  |  |
| 9 | CN50C | Fireproofing treatment of the carpentry, stave-based screen for coverings and revetment. | 100m2 | 9,1200 |  |  |
| 10 | CN51F | Antiseptic treatment of the carpentry, on apparent areas with antiseptic paste: needling, ribs. | 100m2 | 9,1200 |  |  |
| 11 | CE17A | Additional polymeric membrane for anticondens layer, assembled under the tile covering imprinted board plates | m2 | 912,0000 |  |  |
| 12 | RpCH08A | Cornice boarding from aluminum thin boards with angles on the perimeter | m2 | 122,8000 |  |  |
| 13 | RpCH02A | Resinous wooden framing, on simple roofs, with one with up to 4 slopes, for covering from tiling, from square timber, for light roofs (entry dome) | m2 | 26,4500 |  |  |
| 14 | RpCH07A1 | Repairing the revetment of the covering of resinous boards, of 24 mm width, executed via replacement of the broken revetment with boards for usual constructions, for total replacement of the revetment | m2 | 26,4500 |  |  |
| 15 | CE07A | Covering from imprinted board plates (roof tile) for covering the roofs Metallic tiles of "Monterrey" type, thickness 0.5 or equivalent | m2 | 26,4500 |  |  |
| 16 | CK17A | Paneling executed on the site in quantities over 10 m2 from resinous timber, plates (coating the dome) | m2 | 26,4500 |  |  |
| 17 | CE42A | Execution of dormers | piece | 2,0000 |  |  |
| 18 | CB14A | Tubular metallic scaffold for works of vertical areas for heights up to 30 m inclusively, with immobilization of the scaffold for 25 days (200 hours) | m2 | 149,2500 |  |  |
| 19 | TsI50A10 | Transportation of soil with the dumper for a distance of 10 km (transportation of brash) | t | 57,0000 |  |  |
| 20 | RpCU09C | Transportation with manual means through direct transportation up to 60 m distance with a loading up to 50 kg (for 1 m transported on the vertical is considered to be 10 on the horizontal) | t | 57,0000 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total Roof Including salary |  |  |  |  |
|  |  | 1.2. Changing the carpentry |  |  |  |  |
| 21 | RpCO56A | Dismantling of the wooden carpeting (windows) | m2 | 148,6200 |  |  |
| 22 | RpCO56A | Dismantling of the wooden carpeting (doors) | m2 | 120,8770 |  |  |
| 23 | TsI50A5 | Transportation of soil with the dumper for a distance of 5 km (transportation of brash) | t | 6,0000 |  |  |
| 24 | CK23C | Plastic windows with one or more leafs with heights up to 35 m inclusively, having an area of the casement of over 2,5 m2 | m2 | 148,6200 |  |  |
| 25 | CK25A | Doors made of plastic profiles, including the casement and the necessary accessories for assembling doors in any type of constructions with the height up to 35 m inclusively with the surface of the case up to 7 m2 inclusively | m2 | 114,3600 |  |  |
| 26 | RpCP35A | Replacing the window sills of plastic | m | 78,6500 |  |  |
| 27 | RpCP35B | Replacing the window sills of aluminum | m | 78,6500 |  |  |
| 28 | RpCJ06C | Repairing the interior coating, around the cases and casing of the doors and windows, of 2 cm thickness, leveled, executed with cement-lime mortar of type 25 T, with right recesses in between 25 - 35 cm width | m | 323,1300 |  |  |
| 29 | CF61A | Continue levelling of surface (one layer coating) with dry mixture of gypsum: plane window and door jambs (aluminum corner - 330m) | m2 | 210,0400 |  |  |
| 30 | CF57A | Manual application of the gypsum-based putty of type "Eurofin" or equivalent thickness 1,0 mm on the walls, columns, and ceilings (Windows) | m2 | 210,0400 |  |  |
| 31 | CN53A | Coating the interior surface of the ceiling and walls (Windows) | m2 | 210,0400 |  |  |
| 32 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually (windows) | m2 | 210,0400 |  |  |
| 33 | RpCJ06C1 | Repairing the interior coating around the windows’ and doors’ cases, of 2 cm thickness, leveled, executed with cement-lime mortar 25 T, having straight recesses, between 25 - 35 cm width, (doors) | m | 646,2600 |  |  |
| 34 | CF61A | Continue levelling of surface (one layer coating) with dry mixture of gypsum: plane window and door jambs (aluminum profile - 650m) | m2 | 124,6400 |  |  |
| 35 | CF57A | Manual application of the gypsum-based putty of type "Eurofin" or equivalent thickness 1,0 mm on the walls, columns, and ceilings (Doors) | m2 | 124,6400 |  |  |
| 36 | CN53A | Coating the interior surface of the ceiling and walls (Doors) | m2 | 124,6400 |  |  |
| 37 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually (doors) | m2 | 124,6400 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total Changing the carpeting Including salary |  |  |  |  |
|  |  | 1.3. Repairing works for ceilings |  |  |  |  |
| 38 | СF59D | Coating the surfaces with a layer of plasterboards executing the simple plain metallic carcass, with the height up to 4 m: ceilings with insulation | m2 | 140,0000 |  |  |
| 39 | CF57A | Manual application of the gypsum-based putty of type "Eurofin" or equivalent thickness 1,0 mm on the ceiling areas | m2 | 140,0000 |  |  |
| 40 | CN53A | Coating the interior surface of the ceiling | m2 | 140,0000 |  |  |
| 41 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually | m2 | 140,0000 |  |  |
| 42 | CK29F | Suspended ceiling from pre-manufactured panels of type "Armstrong" or equivalent , including the system-grid, 2 floor | m2 | 250,0000 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total Repairing works for the ceiling Including salary |  |  |  |  |
|  |  | 1.4. Repairing works for the walls (partially) |  |  |  |  |
| 43 | CN54A | Manual application of the quartz ground of type "BETONOCONTACT" or equivalent in one layer, for the interior walls | m2 | 282,0000 |  |  |
| 44 | RpCJ12A | Exterior plastering trowel, executed in cement mortar M 100-T of 2 cm average thickness, for walls from concrete or bricks, with plain surfaces | m2 | 282,0000 |  |  |
| 45 | CN53A | Coating the interior surface of the walls | m2 | 200,0000 |  |  |
| 46 | CF50A | Interior coating of 5 mm thickness, executed manually, with gypsum-based dry mixture, at walls and dividing walls, mechanic preparing of the mortar. | m2 | 200,0000 |  |  |
| 47 | CF57A | Manual application of the gypsum-based putty of type "Eurofin" or equivalent thickness 1,0 mm on the wall areas | m2 | 200,0000 |  |  |
| 48 | CN53A | Coating the interior surface of the walls | m2 | 200,0000 |  |  |
| 49 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually | m2 | 200,0000 |  |  |
| 50 | CI06C3 | Plywood with colorful tiles mounted in different colors and shapes mounted in the drawing, executed on flat surfaces of walls and pillars , including sills and edges , with alternating joints, in premises with an area exceeding 10 m2, fixed with adhesive for installation of plywood for proper installation | m2 | 82,0000 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total Repairing works for walls (partially) Including salary |  |  |  |  |
|  |  | 1.5. Repairing works for floor |  |  |  |  |
| 51 | RpCK41C | Dismantling the flooring of PVC coverage on or without textile support, or moquette, etc. | m2 | 730,0000 |  |  |
| 52 | RpCK42A | Dismantling the cold flooring of concrete or cement mortar | m2 | 730,0000 |  |  |
| 53 | TsI50A5 | Transportation of soil with the dumper for a distance of 5 km (transportation of brash) | t | 18,0000 |  |  |
| 54 | CG01A | Supporting layer for flooring executed from cement mortar M 100-T of 3 cm thickness with delicately smoothed face | m2 | 730,0000 |  |  |
| 55 | CG17D | Flooring from ceramic plates including the support layer from adhesive mortar, executed on areas wider than 16 m2 | m2 | 298,8000 |  |  |
| 56 | CG18A | Horizontal plinths with maximum height of 15 cm for the walls out of ceramic plates fixed with cement mortar M 100-T, including the cleaning and washing with water, in premises with areas wider than 16 m2 | m | 320,0000 |  |  |
| 57 | CG08A | Plastic coatings mounted on existing support, cleaned , including PVC skirting boards in premises with areas larger than 16 m2, with PVC carpet soldered with glue | m2 | 69,8000 |  |  |
| 58 | CG56A | Blanket from self-levelling mix of type "Nivelir" or equivalent : thickness 10mm | m2 | 361,4000 |  |  |
| 59 | CG49A | Executing the antibacterial coverage with homogeneous vinyl (medical linoleum) flooring | m2 | 361,4000 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total Repairing works for flooring Including salary |  |  |  |  |
|  |  | 1.6. Pavement |  |  |  |  |
| 60 | RpDB37A k=1.33 | Scouring the asphalt up to 3 cm thick, made of permanent asphaltic carpets, asphaltic cement or asphaltic mortar | m2 | 524,0300 |  |  |
| 61 | TsC02B1 | Mechanic digging with pneumatic excavator of 0,21-0,39 m3, with hydraulic command, in grounds with natural humidity, and unloading on the field storage of cat. II. | 100 m3 | 1,5700 |  |  |
| 62 | TrI1AA02C3 | Loading materials from group A – heavy ones, by throwing balls in – from the ramp or field, in auto category 3 | t | 188,0000 |  |  |
| 63 | TsI50A10 | Transportation of soil with the dumper for a distance of 10 km (transportation of brash) | t | 188,0000 |  |  |
| 64 | RpDD01A | Foundation or re-profiling layer from crushed stone, for roads with manual covering, executed with wedging or renewal | m3 | 52,4000 |  |  |
| 65 | TsC54A | Foundation layer of sand | m3 | 52,4000 |  |  |
| 66 | DE17B | Pavement made of precast concrete paving slabs laid on a layer of dry cement and sand mixture in the proportion 1: 3 , embroidered with dry mixture of cement and sand , 10 cm thick layer of paving | m2 | 524,0300 |  |  |
| 67 | TsA03C | Manual excavation of land in confined spaces , having 1.00 m in width , made without support , with sloping embankment foundations , channels , etc. , cohesive or poorly cohesive, consistent land , up to 0.75 m deep hard ground | m3 | 7,6600 |  |  |
| 68 | CO03A | Edging for sidewalks based on mortar of M 100-T of 5 cm thick, on a concrete foundation, class C 5/4 of about 15 cm thick, with joints filled with mortar | m | 153,3100 |  |  |
| 69 | RpCK42C | Dismantling the floors of cold concrete tiles, marble, stone, ceramic tiles, etc. | m2 | 12,3000 |  |  |
| 70 | RpCL15A | Repairing concrete and mosaic steps on the site, executed roughly and with mosaic made of granulated stone (dosage 600 kg cement per cubic meter of stone mosaic), rubbed, with a 15 mm wear layer | m | 25,9500 |  |  |
| 71 | CG17D | Flooring from ceramic plates “Porcelain for exterior”, including the support layer from adhesive mortar executed on areas wider than 16 m2 | m2 | 25,2700 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total Pavement Including salary |  |  |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Social and health insurance | 27,5 % |  |  |  |
|  |  | Total |  |  |  |  |
|  |  | Transportation costs | % |  |  |  |
|  |  | Direct costs |  |  |  |  |
|  |  | Overhead costs | % |  |  |  |
|  |  | Total |  |  |  |  |
|  |  | Estimate benefit | % |  |  |  |
|  |  | Total General repairing works Including salary |  |  |  |  |
|  |  | 2. Heating |  |  |  |  |
| 72 | RpIF01A | Draining the central heating installation so as to perform the repairing works | m2 | 120,0000 |  |  |
| 73 | RpIC19D | Dismantling the black pipe, for installations, assembled in the central heating installation by welding, in social purpose and dwelling buildings, when linking the distribution devices, columns etc. with a diameter of 2 1/2" -3" | m | 274,3000 |  |  |
| 74 | RpIC19A | Dismantling the black pipe, for installations, assembled in the central heating installation by welding, in social purpose and dwelling buildings, when linking the distribution devices, columns etc. with a diameter of 3/8" - 3/4" | m | 137,5000 |  |  |
| 75 | RpIB11A | Dismantling the radiators to be liquidated | m2 | 120,0000 |  |  |
| 76 | RpIB11C | Dismantling the consoles or the supporting devices for liquidation | piece | 110,0000 |  |  |
| 77 | RpID07A | Assembling the airing taps with valves, with the mobile key with dn=1/2 (Tap –of type Maievsky or equivalent) | piece | 55,0000 |  |  |
| 78 | RpIC35A | Executing the conjunction of steel pipes’ ramifications for constructions, with diameter of 54x3.5-60x3.5 | piece | 5,0000 |  |  |
| 79 | IC10H | Black steel pipe with filet and sleeve assembled through screwing to the distribution pipes of the central heating installation for dwelling and social-cultural buildings, pipe with a diameter of 3" (Passing grips) | m | 6,0000 |  |  |
| 80 | RpCU05G | Executing the perforation for the pipes or ties in the walls of bricks of 26 -50 cm thickness | piece | 120,0000 |  |  |
| 81 | RpCU07B | Caulking the holes in the walls with cement-lime mortar, after installations or consolidations | piece | 120,0000 |  |  |
| 82 | ID04B | Passing or retaining tap with sleeves for central heating installations, having the nominal diameter 2" | piece | 28,0000 |  |  |
| 83 | IC10F | Black steel pipe with fillet and sleeve assembled by being screwed to the distribution pipes, in central heating installation for dwellings and social-cultural purpose buildings, the pipe has the diameter of 2" | m | 374,3000 |  |  |
| 84 | IC10B | Black steel pipe with fillet and sleeve assembled by being screwed to the distribution pipes, in central heating installation for dwellings and social-cultural purpose buildings, the pipe has the diameter of 3/4" | m | 137,5000 |  |  |
| 85 | ID01B | Tap with valve with double control (supply and return) for central heating installations, having the nominal diameter 3/4" -1" | piece | 112,0000 |  |  |
| 86 | IB01A | Cast iron radiators with free columns and circular section or united columns and elliptic section (375.00 sections of type MS 104 or equivalent ) the standard for radiator 3.125 sections/m2 | m2 | 185,6000 |  |  |
| 87 | IB20A | Support elements for the heating bodies, assembled in the brick wall. | piece | 110,0000 |  |  |
| 88 | RpIC28B | Assembling or intercalating on the pipes the fittings, to the existing pipes of central heating (sleeve, nipple, joint, T-joint, plug, reductions, Holland connector, etc.), with diameter 2" | piece | 55,0000 |  |  |
| 89 | IC40A | Bracket for fixing the steel pipes for central heating or gas installation, assembled on gimlets of 1" inclusively, on PVC gimlets on brick walls | piece | 55,0000 |  |  |
| 90 | IC40C | Bracket for fixing the steel pipes for central heating or gas installation, assembled on gimlets of 2 1/2" , on PVC gimlets on brick walls | piece | 61,0000 |  |  |
| 91 | IE01A | Performing the under pressure impermeability testing of the central heating installation, having pipes from steel, copper, polyethylene or polypropylene, with heating bodies, heating devices, fittings, distributors, collectors, reservoirs, and airing taps, with the total area of the heating bodies up to 100 m2 | m2 | 185,6000 |  |  |
| 92 | IE02A | Performing the dilatation – contracting and operation testing of the central heating installation, having pipes from steel, copper, polyethylene or polypropylene, with heating bodies, heating devices, fittings, distributors, collectors, reservoirs, and airing taps, with the total area of the heating bodies up to la 100 m2 | m2 | 185,6000 |  |  |
| 93 | IE08A | Washing with drinking water the internal installation of central heating, the total area of the bodies being up to 100 m2 | m2 | 185,6000 |  |  |
| 94 | CN23A | Paintings of superior quality of the functional installations, executed with oil-based paint on pipes with the exterior diameter up to 34 mm inclusively | m | 315,0000 |  |  |
| 95 | CN23B | Paintings of superior quality of the functional installations, executed with oil-based paint on pipes with the exterior diameter over 34 mm inclusively | m2 | 185,6000 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Social and health insurance | 27,5 % |  |  |  |
|  |  | Total |  |  |  |  |
|  |  | Transportation costs | % |  |  |  |
|  |  | Direct costs |  |  |  |  |
|  |  | Overhead costs | % |  |  |  |
|  |  | Total |  |  |  |  |
|  |  | Estimate benefit | % |  |  |  |
|  |  | Total Heating Including salary |  |  |  |  |
|  |  | 3. Electricity |  |  |  |  |
| 96 | RpEG02A | Mounting the electrical panel on metallic shelves, modulated with mask, on the wall or in the corbel, having an area up to 0,30 m2 (18 modules) | piece | 4,0000 |  |  |
| 97 | RpEE03A | Assembling bipolar sockets in normal constructions from bakelite or amino-plastic, simple, double, water-proof construction, seals, metallic or similar seals, assembled under coating or visibly on the wood or plastic gimlets | piece | 195,0000 |  |  |
| 98 | RpEE01A | Mounting unipolar or bipolar switches 10-25 A, of normal construction, sealed in waterproof aminoplast carcass, bakelite, metal or porcelain recessed or surface mounted on wooden dowels or plastic, with copper connectors | piece | 12,0000 |  |  |
| 99 | RpEE15A | Mounting the monopolar switches 25 A- | piece | 69,0000 |  |  |
| 100 | RpEF15E | Mounting Led fittings, fluorescent type CIT 220 W, without tube (2*18W) | piece | 136,0000 |  |  |
| 101 | RpEF12B | Mounting lamps (bulbs): incandescent, fluorescent tubes | piece | 272,0000 |  |  |
| 102 | RpEA09A | Assembling the protection elements of plastic, on the walls or in the channels, to mask the electricity conductors or cables, with dimensions of 8x21 mm | m | 2 330,0000 |  |  |
| 103 | RpEB01A | Assembling the masked conductors, of copper, in tubes, protection elements, flush mountable, with the section up to 16 mm2 2x1.5 mm | m | 830,0000 |  |  |
| 104 | RpEB01A | Assembling the masked conductors, of copper, in tubes, protection elements, flush mountable, with the section up to 16 mm2 3x4 mm | m | 450,0000 |  |  |
| 105 | RpEB01A | Assembling the masked conductors, of copper, in tubes, protection elements, flush mountable, with the section up to 16 mm2 3x2.5 mm | m | 1 050,0000 |  |  |
| 106 | 08-02-144-3 | Connecting the wires of the conductors or of the cables to the clamps, section up to 16 mm2 | 100 piece | 4,0000 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Social and health insurance | 27,5 % |  |  |  |
|  |  | Total |  |  |  |  |
|  |  | Transportation costs | % |  |  |  |
|  |  | Direct costs |  |  |  |  |
|  |  | Overhead cost | % |  |  |  |
|  |  | Total |  |  |  |  |
|  |  | Estimate benefit | % |  |  |  |
|  |  | Total Electricity Including salary |  |  |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total estimate: Including salary |  |  |  |  |

| Compiled |  |
| --- | --- |
| (position, signature, name, surname) |
| Verified |  |
| (position, signature, name, surname) |