| Repairing works in the Youth Creation Palace from Dubasari city | Form No.7 WinСmeta |
| --- | --- |
| (name of the site) |  |

LOCAL ESTIMATES No 1

Repairing works

Concluded based on current prices as of 01.11.2015

| No | Symbol of the norm and resource code | Works and expenses | U.M. | Quantity according to the design data | Estimate value, lei |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Per U.M. ———— incl. salary | Total ————— incl. salary |

| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | 1. Construction works |  |  |  |  |
|  |  | 1.1. Roof |  |  |  |  |
| 1 | RpCI42B | Dismantling roof elements – asbestos-cement cover and afferent elements | m2 | 1 214,00 |  |  |
| 2 | RpCH32C | Removing the wooden floors and roof elements - deck roof covering with or without recovery of materials | m2 | 1 214,00 |  |  |
| 3 | RpCH13B | Straightening and reinforcing wooden plates with bent beams or those with rotting beams’ edges, with beams from resinous square timber | m3 | 12,40 |  |  |
| 4 | RpCH06E | Repairing the elements of deteriorated framework through consolidation with bolts | kg | 685,00 |  |  |
| 5 | RpCH32D | Removing the wooden boards and roof elements - cornice or visible boarding Parapets | m2 | 48,00 |  |  |
| 6 | RpCH32D | Removing the wooden boards and roof elements - cornice or visible boarding Overhang | m2 | 70,00 |  |  |
| 7 | RpCH32F | Removing the wooden boards and roof elements - Dormer | piece | 2,00 |  |  |
| 8 | RpCH16A | Repairing the flooring between the beams of the wooden joists, executed with resinous boards | m2 | 212,00 |  |  |
| 9 | CE17A | Additional polymeric layer, anticondens membrane, assembled under the tile covering layer, | m2 | 1 214,00 |  |  |
| 10 | RpCH07A1 | Repairing the revetment of the covering of resinous boards, of 24 mm width, executed via replacement of the broken revetment with chipboard for usual constructions, for total replacement of the revetment | m2 | 1 214,00 |  |  |
| 11 | CE07A | Covering from imprinted board plates (Profnastil) of 0,5 mm for roof covering (with the consumption norm- 1,22 m2/1 m2 of roof) | m2 | 1 214,00 |  |  |
| 12 | CN50A | Fireproof treatment of the carpentry; trusses, arches, beams, rafters, plates. | m3 | 44,50 |  |  |
| 13 | CN51D | Antiseptic treatment of the carpentry, on hidden areas with antiseptic paste: beams, plates. | m3 | 44,50 |  |  |
| 14 | RpCH08B | Cornice boarding from resinous boards rasped and rabbeted on one side, with the initial thickness of 24 mm, rasped on both side with apparent consoles, rasped and profiled. Wooden panels | m2 | 70,00 |  |  |
| 15 | CE31A | Fascia for eaves or gables of profiled plates (the “Profnastil” tile norm 1.2 m2) | m2 | 19,20 |  |  |
| 16 | CN16D | Painting with oil-based paints applied on the carpentry, executed with 2 layers of enamel for decking | m2 | 70,00 |  |  |
| 17 | CL17B | Various metal garments, mounted visibly: snow stops | kg | 89,60 |  |  |
| 18 | CE20A | Systems of brass-type ditches from anticorrosive protected board d=150 mm rain downpipe | m | 95,00 |  |  |
| 19 | CE22A | Systems of brass-type tubing from anticorrosive protected board rain gutter | m | 78,00 |  |  |
| 20 | CE42A | Execution of dormers | piece | 3,00 |  |  |
| 21 | IzF10H | Insulating layer for terraces, roofs and floors, from slabs and mats of insulating material with reduced embedded energy (waste , flax, hemp, etc.) simply laid in dry bridges, not-circulated on horizontal or sloping surfaces up to 20% boards of mineral wool b 100mm | m2 | 970,00 |  |  |
| 22 | CE31A | Fascia for eaves or gables of simply smoothed boards (ventilation channels) | m2 | 32,00 |  |  |
| 23 | CB14A | Tubular metallic scaffold for works of vertical areas for heights up to 30 m inclusively, with immobilization of the scaffold for 25 days (200 hours) (eaves and gables) | m2 | 112,00 |  |  |
| 24 | TsI50A5 | Transportation of the ground with the dumper at a distance of 5 km | t | 156,20 |  |  |
|  |  | Total | Lei | Lei |  |  |
|  |  | Total Roof Including salary |  |  |  |  |
|  |  | 1.2. External carpentry and sills |  |  |  |  |
| 25 | RpCO56A | Dismantling of the wooden carpeting (windows) | m2 | 84,00 |  |  |
| 26 | RpCO56A | Dismantling of the wooden carpeting (doors) | m2 | 28,61 |  |  |
| 27 | RpCO28B | Making door plates, exterior, simple, on existing case, from resinous timber, in two leaves (re-establishing the entry door) | m2 | 8,20 |  |  |
| 28 | CN16A | Painting with oil-based applied on the carpentry from wood, executed with 3 layers of oil-based paints for doors and windows already with primer. | m2 | 16,40 |  |  |
| 29 | CK25A | Doors made of plastic profiles, including the casement and the necessary accessories for assembling doors in any type of constructions with the height up to 35 m inclusively, in one wing, with the surface of the case up to 7 m2 inclusively (exterior doors) | m2 | 21,70 |  |  |
| 30 | CK12A | Metallic doors manufactured from rolled iron profiles, steel-band cold-cut profiles, including necessary coat and accessories for the doors assembled in walls of any type of construction, with height up to 35 m inclusively, within one leaf, with the area of the case between 7 m2 inclusively | m2 | 6,90 |  |  |
| 31 | CK23C | Plastic windows with one or more leafs with heights up to 35 m inclusively, having an area of the casement of over 2,5 m2 profile with 5 chambers, low-E glass | m2 | 84,00 |  |  |
| 32 | CK26A | Sills assembled at the windows from plastic, for windows | m | 47,30 |  |  |
| 33 | CK26D | Sills assembled at the windows or doors from aluminum | m | 47,30 |  |  |
| 34 | RpCJ06C1 | Repairing the interior coating, around the cases and casing of the doors and windows, of 2 cm thickness, leveled, executed with cement-lime mortar of type 25 T, with right recesses in between 25 - 35 cm width, for curb surfaces (internal ones) | m | 142,50 |  |  |
| 35 | CF50B | Interior coating of 5 mm thickness, executed manually, with gypsum-based dry mixture, for walls and dividing walls, manual preparation of the mortar. | m2 | 57,00 |  |  |
| 36 | CN53A | Coating the external surfaces of the walls | m2 | 57,00 |  |  |
| 37 | CF57A | Manual application of the gypsum-based putty "Eurofin" or equivalent thickness 1,0 mm on the ceiling, walls and columns’ areas. | m2 | 57,00 |  |  |
| 38 | CN53A | Coating the external surfaces of the walls | m2 | 57,00 |  |  |
| 39 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually. | m2 | 57,00 |  |  |
| 40 | CF61A | Continue levelling of surface (one layer of coating with thickness of 1 cm) with dry mixture of gypsum: plane window and door jambs, including priming and aluminum angle (external window sills, dry mix for external works) | m2 | 79,00 |  |  |
| 41 | CN06A | Exterior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually. | m2 | 79,00 |  |  |
| 42 | TsI50A5 | Transportation of the ground with the dumper at a distance of 5 km | t | 23,50 |  |  |
|  |  | Total | Lei | Lei |  |  |
|  |  | Total External carpentry and sills Including salary |  |  |  |  |
|  |  | 1.3. Facade |  |  |  |  |
| 43 | RpCJ35A | Dismantling exterior plastering coating from the walls | m2 | 1 236,00 |  |  |
| 44 | RpCN12B | Dismantling the profiles, shapes or ornaments made on the spot or pre-manufactured, for walls and ceilings, made on the spot with levelled templates or on Rabitz plastering of 0.61 to 1.20 m width | m | 143,20 |  |  |
| 45 | RpCR30A | Exterior painting based on anti-mold substances | m2 | 89,00 |  |  |
| 46 | CN53A | Coating the external surfaces of the walls with concrete primer | m2 | 1 236,00 |  |  |
| 47 | CF15A | Exterior plastering trowel, executed manually with cement mortar M 100-T of 2 cm average thickness, for walls from concrete or bricks, with plain surfaces | m2 | 1 236,00 |  |  |
| 48 | IzF54A | External insulation of buildings with fine plaster on thermal insulation (rigid fixation systems of the thermal insulation), smooth wall surface: with mineral wool 10 cm thickness, a density higher than 135 kg/m3, with dips framing using the mineral wool | m2 | 1 236,00 |  |  |
| 49 | CN54B | Manual application of the quartz ground “Gleta" or equivalent in one layer, for the exterior walls of the facade. | m2 | 1 236,00 |  |  |
| 50 | CF30A | Exterior coating of 2-3 mm thickness, executed manually, with “TINC” or equivalent mixture on the walls. | m2 | 1 236,00 |  |  |
| 51 | RpCM33E | Dismantling the PVC plates the arch key of the main access | m2 | 42,50 |  |  |
| 52 | CN53A | Coating the external surfaces of the walls with concrete primer | m2 | 42,50 |  |  |
| 53 | RCsJ14A1 | Repairing interior coating, smoothed, for ceiling, arch key, arches and domes from brick or reinforced concrete, monolith or pre-manufactured, executed with cement-lime mortar M 100-T for sprit and lime-cement mortar M 25-T for the ground and continuously visible layer (1.5 cm thickness), to remake totally the coating | m2 | 42,50 |  |  |
| 54 | CN53A | Coating the external surfaces of the walls with concrete primer | m2 | 42,50 |  |  |
| 55 | CN11A | Exterior painting with paints based on vinyl copolymers in water emulsion, applied in 3 layers on the facade executed on the existing sill and existent arch keys | m2 | 42,50 |  |  |
| 56 | RCsN05A | Repairing profiles drawn on the site, based on the specific template, for the exterior straight cornices, with width up to 0.75 m unfolded, executed on masonry or concrete with cement mortar lime M 50-T , fine leveled. Reestablishing the decorative elements. | m | 134,00 |  |  |
| 57 | RpCN03A | Repairing profiles drawn on the site, based on the specific template, at the belts, window sills, straight border halls, with width up to 30 m unfolded, executed on masonry or concrete with cement mortar lime M 50-T , fine leveled. | m | 168,75 |  |  |
| 58 | RpCJ35B | Discomposing the special exterior coating in stone dust, mosaic, etc. | m2 | 176,30 |  |  |
| 59 | RpCB18B | Demolishing the old concrete with manual means, foundations and elevations with a dosing up to 150 kg/mc (back stairs) | m3 | 9,51 |  |  |
| 60 | TsC54C | Gravel layer gr 40 100 mm | m3 | 9,40 |  |  |
| 61 | TsD05A | Compaction with the mechanical knocker of 150-200 kg filling in the successive layers of 20-30 cm thickness, excluding the watering of every layer separately, the earth fillings being executed from non-cohesive ground | 100 m3 | 0,94 |  |  |
| 62 | CB01A | Formwork of resinous wood boards, for pouring the monoliths concrete between prefabricated elements (slabs, beams and diaphragms ) including support | m2 | 48,40 |  |  |
| 63 | CA03A2 | Cast concrete slabs , beams , columns , prepared with the concrete plant and pouring with classical means of reinforced concrete Class C 5/4 ( Bc 5/B 75 ) | m3 | 9,51 |  |  |
| 64 | CO07A | Steel metal fencing form profiling steel, ordinary model | kg | 196,70 |  |  |
| 65 | CN21A | Painting the railings, grids and railing, executed with oil paints in 2 layers | m2 | 58,50 |  |  |
| 66 | CC03A | Assembling sealed meshes at heights lower or equal to 35 m, for walls with diaphragms, with the wright of the meshes up to 3 kg/m2 | kg | 198,70 |  |  |
| 67 | CG01A | Supporting layer for flooring executed from cement mortar M 150-T of 2.5 cm thickness with delicately smoothed face | m2 | 87,90 |  |  |
| 68 | RpCJ20A | Repair of exterior plaster on wire-based braids, without reinforcement or steel frames, with the thickness of 3 cm, executed in a leveled manner, in 3 layers, lime-cement mortar 25 -T brand, for HRMS on Rabitz plastering of 1 cm thick, the primer of 1.5 cm and 0.5 cm for the visible layer, applied to the soil-based walls or the walls from bricks built with soil-based mortar | m2 | 176,30 |  |  |
| 69 | CI21A | Plating the walls with Cosauti type plates: size up to 400 x 400 mm. Basement (Cosauti type plates) | m2 | 33,10 |  |  |
| 70 | RpCM17A | Plywood with porcelain tiles glazed , matte or glossy , made surfaces at stairs, with tiles of the same shape and color, having an area up to 60 cm² / pc with alternating grooves filled with white grout for areas larger than 10 m2, fixed with lime-cement M 100 -T on support layer of 2 cm of mortar (exterior porcelain 10mm) | m2 | 89,00 |  |  |
| 71 | CL18A | Diverse metallic confections from rolled profiles, plate, checker plate, steel, concrete, pipes for supporting or covering, totally or partially embedded in concrete (carcasses for the key arch) | kg | 52,80 |  |  |
| 72 | CK29E | Suspended ceilings of prefabricated panels from galvanized steel or aluminum profiles arranged in cells (filling in the exterior key arch with titles of type Etalbond) | m2 | 52,80 |  |  |
| 73 | TsI50A5 | Transportation of the ground with the dumper at a distance of 5 km | t | 156,20 |  |  |
| 74 | CB14A | Tubular metallic scaffold for works of vertical areas for heights up to 30 m inclusively, with immobilization of the scaffold for 25 days (200 hours) | m2 | 1 236,00 |  |  |
|  |  | Total | Lei | Lei |  |  |
|  |  | Total Facade Including salary |  |  |  |  |
|  |  | 1.4. Heating |  |  |  |  |
| 75 | RpIF01A | Draining the central heating installation so as to perform the repairing works | m2 | 150,00 |  |  |
| 76 | RpIC19B | Dismantling the black pipe, for installations, assembled in the central heating installation by welding, in social purpose and dwelling buildings, when linking the distribution devices, columns etc. with a diameter of 1" -1 1/4" | m | 1 000,00 |  |  |
| 77 | RpIC37B | Cutting the steel pipe for installations, with acetylene welding flame, with diameter of 1"-2" | piece | 50,00 |  |  |
| 78 | RpID19A | Dismantling the taps of fittings from cast iron or steel for central heating installations, with diameter up to 2" | piece | 12,00 |  |  |
| 79 | RpIB11A | Dismantling the radiators to be liquidated | m2 | 105,00 |  |  |
| 80 | IC36E | High density reinforced polyethylene or reinforced or non-reinforced polypropylene pipe, mounted in columns at the central heating installations, with the external diameter of 50.0 mm | m | 300,00 |  |  |
| 81 | IC36D | High density reinforced polyethylene or reinforced or non-reinforced polypropylene pipe, mounted in columns at the central heating installations, with the external diameter of 40.0 mm | m | 250,00 |  |  |
| 82 | IC36B | High density reinforced polyethylene or reinforced or non-reinforced polypropylene pipe, mounted in columns at the central heating installations, with the external diameter of 25.0 mm | m | 250,00 |  |  |
| 83 | IC36A | High density reinforced polyethylene or reinforced or non-reinforced polypropylene pipe, mounted in columns at the central heating installations, with the external diameter of 20.0 mm inclusively | m | 200,00 |  |  |
| 84 | RpIF09B1 | Insulating the tubes with heating-insulating sleeves, longitudinally cut, with the diameter and thickness from D=25 mm | m | 130,00 |  |  |
| 85 | RpIF09B1 | Insulating the tubes with heating-insulating sleeves, longitudinally cut, with the diameter and thickness from D=40 mm | m | 65,00 |  |  |
| 86 | IE03A | Performing the leakage test under pressure for the conducts supplying the heating appliances (heaters, thermo-convectors, baseboard convectors, etc.) having a diameter of 3/8 " ... 1" | m | 550,00 |  |  |
| 87 | IE03B | Performing the leakage test under pressure for the conducts supplying the heating appliances (heaters, thermo-convectors, baseboard convectors, etc.) having a diameter of 1 1/4 " ... 2" | m | 450,00 |  |  |
| 88 | IB06A | Steel radiators, mono-blocks with the length up to 1000x500 mm | piece | 8,00 |  |  |
| 89 | IB06C | Steel radiators, mono-blocks with the length of 2000x500 mm | piece | 33,00 |  |  |
| 90 | IE02A | Performing the under pressure impermeability testing of the central heating installation, having pipes from steel, copper, polyethylene or polypropylene, with heating bodies, heating devices, fittings, distributors, collectors, reservoirs, and airing taps, with the total area of the heating bodies up to 100 m2 | m2 | 125,00 |  |  |
| 91 | ID04A | Passing or retaining tap with sleeves for central heating installations, having the nominal diameter 1/2" -16 mm” return tap | piece | 41,00 |  |  |
| 92 | ID04A | Passing or retaining tap with sleeves for central heating installations, having the nominal diameter 1/2" -16 mm” return tap | piece | 41,00 |  |  |
| 93 | ID06A | Airing tap with mobile key for central heating installations, having the nominal diameter 1/4" Maiebschi-type tap | piece | 41,00 |  |  |
| 94 | ID03B | Plug valve tap with three ways, flanges with stuffing, for central heating installations, having a nominal diameter of 25-50 mm (40mm) | piece | 4,00 |  |  |
| 95 | ID04A | Passing or retaining tap with sleeves for central heating installations, having the nominal diameter 25 mm | piece | 12,00 |  |  |
| 96 | ID04A | Passing or retaining tap with sleeves for central heating installations, having the nominal diameter 20 mm, for draining | piece | 3,00 |  |  |
| 97 | IC41B | Bracket for fixing the steel pipes for central heating or gas installation, assembled through shooting, the pipe having 1 1/4" - 2" | piece | 150,00 |  |  |
| 98 | RpCU05D | Executing the perforation for the pipes or ties in the walls of bricks of 16 25 cm thickness | piece | 42,00 |  |  |
| 99 | RpCU07C | Caulking the holes in the plates with cement-lime mortar, after installations | piece | 28,00 |  |  |
|  |  | Total | Lei | Lei |  |  |
|  |  | Total Heating Including salary |  |  |  |  |
|  |  | 1.5. Partial interior finishing works |  |  |  |  |
| 100 | CK29F | Suspended ceiling from pre-manufactured panels "Armstrong", including the system-grid second floor | m2 | 215,00 |  |  |
| 101 | RpCJ35A | Dismantling interior plastering coating from the walls | m2 | 450,00 |  |  |
| 102 | CN54A | Manual application of the quartz ground "BETONOCONTACT" or equivalent in one layer, for the interior walls | m2 | 450,00 |  |  |
| 103 | CF15A | Interior plastering trowel, executed manually with cement mortar M 100-T of 2 cm average thickness, for walls from concrete or bricks, with plain surfaces | m2 | 450,00 |  |  |
| 104 | CF50B | Interior coating of 5 mm thickness, executed manually, with gypsum-based dry mixture, for walls and dividing walls, manual preparation of the mortar. | m2 | 450,00 |  |  |
| 105 | CF57A | Manual application of the gypsum-based putty "Eurofin" oe equivalent thickness 1,0 mm on the walls’ areas. | m2 | 450,00 |  |  |
| 106 | CN06A | Interior painting with paints based on vinyl copolymers in water emulsion, applied in 2 layers on the existing fillings, executed manually. | m2 | 450,00 |  |  |
| 107 | CK30B | Ready-made mask for the radiators manufactured from wooden or aluminum board rods, including gimlets | m2 | 87,50 |  |  |
| 108 | RpCK10C | Oak parquetry scraping , executed mechanically, with abrasive disks | m2 | 215,00 |  |  |
| 109 | RpCK10C | Oak parquetry scraping , executed mechanically, with abrasive disks | m2 | 215,00 |  |  |
| 110 | CG06A | Oak plinths cleaned and assembled on wooden dowels fixed with brass screws in premises with areas larger than 16 m2, horizontal plinths with maximum height of 15 cm for walls | m | 162,00 |  |  |
|  |  | Total | Lei | Lei |  |  |
|  |  | Total Partial interior finishing works Including salary |  |  |  |  |
|  |  | 1.6. WC |  |  |  |  |
| 111 | CK17F | Paneling the walls, executed on the site in quantities of over 10 square meters of plastic profiles | m2 | 8,25 |  |  |
| 112 | RpCJ35A | Dismantling interior plastering coating from the walls | m2 | 32,50 |  |  |
| 113 | CN54A | Manual application of the quartz ground "BETONOCONTACT" or equivalent in one layer, for the interior walls | m2 | 32,50 |  |  |
| 114 | CF15A | Interior plastering trowel, executed manually with cement mortar M 100-T of 2 cm average thickness, for walls from concrete or bricks, with plain surfaces | m2 | 32,50 |  |  |
| 115 | CI06C3 | Plywood with colorful tiles mounted in different colors and shapes mounted in the drawing, executed on flat surfaces of walls and pillars , including sills and edges , with alternating joints, in premises with an area exceeding 10 m2, fixed with adhesive for installation of plywood | m2 | 32,50 |  |  |
| 116 | RpCK42A | Dismantling the cold flooring from concrete and cement mortar | m2 | 8,25 |  |  |
| 117 | CG01A | Supporting layer for flooring executed from cement mortar M 100-T of 3 cm thickness with delicately smoothed face | m2 | 8,25 |  |  |
| 118 | CG17D1 | Flooring from ceramic plates, including the support layer from adhesive mortar executed on areas equal to or smaller than 16 m2 Betonocontact Fixing - 0.3 kg/m2 | m2 | 8,25 |  |  |
| 119 | RpSB10C | Assembling the non-plasticized light PVC pipe for sewerage, joined by gluing, surface-mounted or buried under the floor, with the diameter of 50 mm | m | 5,00 |  |  |
| 120 | RpSB11B | Mounting the connecting pipe (bend) from the light type PVC pipe, joined by gluing, with the diameter of 50 mm | piece | 2,00 |  |  |
| 121 | RpSB10E | Assembling the non-plasticized light PVC pipe for sewerage, joined by gluing, surface-mounted or buried under the floor, with the diameter of 110 mm | m | 3,00 |  |  |
| 122 | RpSB11D | Mounting the connecting pipe (T-bend) from the light type PVC pipe, joined by gluing, with the diameter of 110 mm | piece | 2,00 |  |  |
| 123 | SB09E | Plastic T-bend for sewerage, combined with rubber, with the diameter of 110 mm | piece | 2,00 |  |  |
| 124 | RpID28B | Mounting the ball-shaped tap with the exterior-interior valve on the copper pipes to the central heating installation, with the diameter 20 mm | piece | 2,00 |  |  |
| 125 | RpSC24B | Mounting the closet reservoir, completely equipped, from sanitary porcelain etc. including for disabled people, placed on the floor, with the water reservoir mounted at a certain height, with the P-type internal siphon | piece | 2,00 |  |  |
| 126 | RpSC21C | Mounting the sink from sanitary semi-porcelain or porcelain, etc. including for disabled people, with the sewerage pipe of plastic material, mounted on a pedestal | piece | 2,00 |  |  |
| 127 | RpSD35A | Mounting the static mixing battery for the washbasin or sink, regardless of the switch-off model, including for disable people, with the diameter of 1/2" | piece | 2,00 |  |  |
| 128 | TsA03E | Manual excavation of land in limited spaces, under 1,00 m width, executed without supporters, with sloping embankment, channels, etc., middle or high cohesion ground, up to 1,5 m deep, middle ground | m3 | 3,00 |  |  |
| 129 | RpSB10E | Assembling the non-plasticized light PVC pipe for sewerage, joined by gluing, surface-mounted or buried under the floor, with the diameter of 110 mm | m | 12,00 |  |  |
| 130 | 08-03-591-2 | Switcher with one flap, unburied type, in open installation | 100 pieces | 0,02 |  |  |
| 131 |  | Boxes for installation of plugs and switches | piece | 2,00 |  |  |
| 132 | 5901034 | Cable VVGng -2*1,5mm | m | 35,00 |  |  |
| 133 | Market price | Light fitting 1x50w QBD | piece | 3,00 |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total WC Including salary |  |  |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Social and health insurance | 27.5 % |  |  |  |
|  |  | Direct cost | % |  |  |  |
|  |  | Direct cost |  |  |  |  |
|  |  | Total | % |  |  |  |
|  |  | Total |  |  |  |  |
|  |  | Estimate benefit | % |  |  |  |
|  |  | Total Construction works Including salary |  |  |  |  |
|  |  | Total | Lei |  |  |  |
|  |  | Total estimates: Including salary |  |  |  |  |

| Compiled |  |
| --- | --- |
| (position, signature, name, surname) |
| Verified |  |
| (position, signature, name, surname) |